## Slide 1: OCP-TAP LET'S TALK SERVOS

## Slide 2: INTRODUCTION
Page 2
Clock synchronization is essential in numerous applications, ranging from telecommunications and network protocols to industrial automation and financial transactions
Accuracy of synchronized clocks is paramount, as deviations in timekeeping can lead to:
  data inconsistencies
  communication errors
  operational disruptions
Servos (servomechanisms) play a critical role in achieving accurate clock synchronization

## Slide 3: TIME, PHASE & FREQUENCY
We all know what time is - unit is second [s]
Phase is the angle of a rotating vector; in clock terms: time related to the period of a repetitive signal - unit is radians [rad] Frequency is a statistical term; number of events per second - unit is Hertz [Hz]
phase
frequency increase
phase increase
frequency
t
Page 3

## Slide 4: THERE ARE TWO “THINGS” TO SYNCHRONIZE
Frequency and Time
Frequency
Time/Phase
BITS in
Output Data
Output Data
Output Data
205-12#sh clock
*13:38:54.805 UTC Mon Apr 2 2012
Page 4
BITS … Building Integrated Timing Supply

## Slide 5: WHAT IS “SYNCHRONIZATION”
125MHz + x PPM Counter 125MHz + y PPM Counter | Count Time | Not Synchronized
125MHz + x PPM Counter 125MHz + x PPM PLL Counter | Count Time | Frequency Synchronized (Syntonised)
125MHz + x PPM Counter 125MHz + x PPM Clear (1 PPS) PLL Counter 1PPS = 1 Pulse Per Second | Count Time | Phase/Time Synchronized
Page 5

## Slide 6: FREQUENCY SYNCHRONIZATION
Page 6

## Slide 7: FREQUENCY SYNCHRONIZATION
Two clocks are frequency synchronized if the frequency of the two clocks have common denominator.
Two clocks are called plesiochronous if the difference in their common denominator is bounded.
The difference in position of rising edges of the clocks is called phase offset.
Two common frequencies which have constant phase offset are phase-locked and implicitly frequency synchronized.
A
System A
B
System B
Reference timing signal
to system A
Reference timing signal to system B
:N
:M
Common f
θ
θ = phase offset of signal from system B
relative to signal from system A
Page 7

## Slide 8: PHYSICAL LAYER FREQUENCY DISTRIBUTION
CDR … Clock Data Recovery; NE … Network Element
NE clock
CDR
time (t)
t(n1)
t(n)
t(n1)
Rate: 8 kHz to 100’s of MHz
Page 8
The timing signal is typically implemented as a periodic digital
signal.

## Slide 9: SIGNIFICANT INSTANTS – PHYSICAL DISTRIBUTION
Timing Signal and Noise
Timing jitter and wander
Time
Timing signal
Significant instants
G.8260(10)_F04
Source: ITU-T G.8260 (202211)
Example : 25 MHz signal
TIE … Time Interval Error
Page 9
Rate: 8 kHz to 100’s of MHz

## Slide 10: PACKET-BASED FREQUENCY DISTRIBUTION
Three key steps:
  Generation: from physical signal to packet
  Transfer: timing events (frame or packet flow) transmission over packet network
  Recovery: from packet-based signal to physical signal
Reference Clock
Recovered Clock
Packet-based timing Flow
Adaptive Clock Recovery (ACR) using IEEE1588 Precision Time Protocol (PTP)
Packet
master
Packet slave

## Slide 11: SIGNIFICANT INSTANTS PACKET-BASED DISTRIBUTION
Timing signal could either be
  Periodic with known send frequency (e.g., CES) or
  With additional information (e.g., PTP timestamps) defining the ideal position in time of the significant instant relative to a master time scale.
Significant instants
Source: ITU-T G.8260 (202211)
CES … Circuit Emulation Service; PTP … Precision Time Protocol
G.8260(10)_F05
F Payload H
Packet delay variation
Event packets (header, payload and footer)
Time
F Payload H
F Payload H
F Payload H
Rate : typical 1-64 Hz
Packet Delay Variation (PDV) of IEEE 1588 un-aware wide area network
Delay
Time
PDV profiles per ITU-T G.8261 Appendix VI
Page 11

## Slide 12: PACKET-BASED TIMING RECOVERY
2. Select the “good” packets depending on network conditions
3. Process the “good” packets to recover clock
Three Major Tasks:
1. Classify the packets
XO … Oscillator; PLL … Phase Locked Loop; PDV … Packet Delay Variation
Reference Clock
Recovered Clock
Packet-based timing Flow
Packet master
Packet slave
Packet selection
PLL
XO
Local reference
Servo
Source: ITU-T G.8260 (202211)

## Slide 13: TIME SYNCHRONIZATION

## Slide 14: TIME – A CLOSER LOOK
Time = Phase + Time of Day
1PPS Pulse  Phase
(analog signal on the DIN connector)
Time of Day (TOD) Information
(serial interface on the RJ45 connector)
*13:38:54.805 UTC Mon Apr 2 2012

## Slide 15: TIME DISTRIBUTION
Packet Layer distributing Phase & Time of Day
00:00:02
00:00:01
00:00:00
ToD messages
Pulse per Second
time
Time Source ToD & 1PPS
Recovered Time ToD & 1PPS
00:00:02
00:00:01
00:00:00
ToD messages
Pulse per Second
time
IEEE1588 PTP Exchange
Master
Slave
Phase Offset

## Slide 16: SYNCHRONIZATION PROTOCOLS

## Slide 17: TWTT PROTOCOL BASICS
Basic PTP Message Exchange
Timestamps known by slave
t1, t2, t3, t4
Delay
Delay
Offset = TS - TM
t1, t2, t3
t1, t2
Delay - Offset = B = t4 – t3
t2 = t1 + Offset + Delay
Offset + Delay = A = t2 – t1
t4 = t3 - Offset + Delay
Master time = TM
Slave time = TS = TM + offset
Offset = ((t2 – t1)–(t4 – t3))/2
Delay = ((t2 – t1)+(t4 – t3))/2
MASTER
SLAVE
Delay_Resp
t1
t4
t2
t3
SYNC
Delay_Req
TWTT … Two-Way Time Transfer

## Slide 18: WHAT IS PRECISION TIME PROTOCOL (PTP)?
Protocol defined by the IEEE in standard 1588-2008 (v2) or 1588-2019 (v2.1)
Profile (how to configure the protocol and what optional features to use, if applicable) defined by the ITU-T in recommendation G.8265.1 (SOOC), G.8275.1 (FTS) or G.8275.2 (APTS/PTS)
  Other industries define their own profiles
An OC or BC with a PTP port in the SLAVE state must synchronize its local
PTP clock to the GM clock – but means of synchronization is
outside scope of
IEEE standard (and sometimes not even mentioned in the Profile)
PRTC/T-GM
IEEE 1588
Slave
IEEE 1588
Slave
T-BC
T-BC
T-BC
T-BC
T-BC
T-BC
T-TSC
T-TSC
IEEE Std 1588™-2019
E.g., High-Stability XO
E.g., Uncompensated XTAL/MEMS
E.g., Precision Measurement
E.g., Precision Servo
FTS … Full Time Support; PTS … Partial Time Support; APTS … Assisted PTS

## Slide 19: I REPEAT, 1558 IS A PROTOCOL
The biggest misunderstand of what 1588 provides is time or clock “synchronization” – precision vs accuracy
It’s a time/clock distribution protocol, but by itself, it only provides a measurement of time/phase offset at a specific instance of sending and receiving an event packet
Looking a tradition PLL model, all PTP provides is the function of the phase/frequency detector (PFD)
You still need a servo!
IEEE Std 1588™-2019

## Slide 20: TYPICAL LINUX PTP IMPLEMENTATION
Packet Switched Network
PHC
Infrastructure
SO_TIMESTAMPING
Socket Option
Protocol Stack
Kernel Driver
PTP
Master Clock
PTP timestamps PHC APIs
Kernel Driver
MAC
Hardware TSU
TODTSU
Servo
Linux PTP v4.0
Linux Kernel
User Space
Digital Control
Local Oscillator

## Slide 21: PHASE-LOCKED LOOP (PLL)
… A CONTROL SYSTEM THAT GENERATES AN OUTPUT SIGNAL WHOSE PHASE IS RELATED TO THE PHASE OF AN INPUT SIGNAL. THERE ARE SEVERAL DIFFERENT TYPES; THE SIMPLEST IS AN ELECTRONIC CIRCUIT CONSISTING OF A VARIABLE FREQUENCY OSCILLATOR AND A PHASE DETECTOR IN A FEEDBACK LOOP. WIKIPEDIA

## Slide 22: WHAT DOES A PLL DO?
Generate a clock that is phase and frequency locked to an input clock.
The output clock frequency can be of the same frequency, an integer multiple or a fraction of the input clock frequency.
Input edge to output edge phase alignment can be achieved.
Input clock frequency to output clock frequency ratio must be a positive integer or fractional number.
19.44 MHz to 66/64*255/237*78125/77760*622.08 MHz is possible.
10 MHz to π MHz is not possible (afaik).
Phase Comparator
Loop Filter
Voltage Controlled Oscillator
uIN (t)
uOUT (t)
uIN (t)  A sin2NOM t  xIN t   A sin2IN t   0,IN 
uOUT (t)  A sin2NOM t  xOUT t   A sin2OUT t   0,OUT 
u
P
 K
P

NOM

x
IN
x
OUT

u
C
(t)  u
P

t

g

t


OUT
 u
C
K
V

0
ref
fb Phase detector
clk
Loop Filter
Digital Controlled Oscillator
Input clock
output clock
sample clock
divider

## Slide 23: PLL BUILDING BLOCKS: PHASE COMPARATOR
The Phase Comparator establishes the “error” between the reference input and the clock output; using a feedback
Most Digital PLLs (DPLLs) use a Time to Digital Converter (TDC) for the Phase Frequency Detector (PFD) to measure the phase of the two clocks and produce a digital word representing the error
TDC can be looked at as a timestamper, resolution determined by the sampling clock
The TDC timestamps the reference and feedback edges, and the PFD mathematically tracks the phase offset between the selected reference and feedback clocks
The measured phase difference can go well beyond 1 period, or Unit Interval (UI), of the reference and feedback clocks; thus, the phase comparator must be able to measure over a large range of multiple input/feedback clock periods
Various telecom standards define a jitter & wander tolerance requirement - the widest is defined is 18µsp-p
For example, if the input clock has a nominal period of 8ns (125 MHz), then the jitter tolerance requirement equates to ± 1125 UI
Ref (In)
Feedback (from Controlled Oscillator)
Phase Error (to Loop Filter)

## Slide 24: PLL BUILDING BLOCKS: LOOP FILTER
The phase error is processed by the loop filter (LF)
LF is a combination of proportional and integral (PI) control, which generates a control signal for controlling the oscillator
The integrator is an additional pole, therefore 2nd order (may be referenced as “Type 2” PLL) The LF determines the bandwidth (BW) of the PLL (i.e. cut-off frequency)
Other functionality, such as phase slope limiting (PSL), locking range, and holdover functionality may be done as well The step response has an overshoot and the frequency domain transfer function has peaking.
Phase corrections mainly done through proportional path, along with any PSL
Frequency offset, or drift corrections, is done through the integrator path, including damping (i.e. gain peaking control)
Control Signal (to Controlled Oscillator)
Phase Error (from Phase Comparator)

## Slide 25: PLL BUILDING BLOCKS: CONTROLLED OSCILLATOR
The controlled oscillator uses the control signal to speed up or slow down the output clock
Most Digital PLLs replace the Voltage Controlled Oscillator (VCO) by a Digitally Control Oscillator (DCO) consisting of:
a free-running crystal oscillator (XO)
A digital synthesizer which pulls the frequency up or down using a Control Signal from loop filter (a digital word representing a fractional frequency offset (FFO))
Clock (Out)
Feedback (to Phase Comparator)
Control Signal (from Loop Filter)
‘Frequency Puller’
Free-running Oscillator
Replaces the VCO
DCO: Digitally Controlled Oscillator

## Slide 26: TYPE 2 DPLL
detector
ref
fb Phase
clk
Digital Controlled Oscillator
Input
clock
output clock
sample clock
centre freq.
integrator
+
Loop Filter
proportional
A loop filter with an additional integrator is inserted.
The integrator is an additional pole, therefore 2nd order.
The DCO pole and the transfer function constants of the PFD and DCO act as a low pass filter.
The jitter transfer function has only 20dB/dec roll-off.
Type 2 DPLL. A non-zero delta freq. no longer requires a non-zero phase offset. So at a non-zero frequency offset the DPLL will lock with zero phase offset.
The step response has an overshoot and the frequency domain transfer function has peaking.
Tau
output clock freq. change
t
phase
f
G[dB]
20dB/dec
peaking
overshoot

## Slide 27: PLL: USE WITH PACKET CLOCKS
A timing protocol, such as IEEE 1588, can be used as the phase (or time) comparator
Still follows same model as PLL, but may introduce a packet selection block
Without packet selection, the packet delay variation (PDV) will have a significant impact to the loop filter The LF will typically be designed to support much lower update intervals of the phase error
This is due to packet dropping, or to attenuate the impact of the PDV
Typically requires a more stable local clock source (oscillator, or maybe physical layer assistance)

## Slide 28: PLL MODES: LOCKED, HOLDOVER AND FREERUN
Freerun mode; the DPLL does not track any input clock. The output clock is at the centre frequency, offset is zero.
i.e. switch is open.
Normal / Lock mode; the DPLL tracks the input clock. The output clock is phase & frequency locked to the input clock.
  i.e. switch is in position 1.
Holdover mode; Typically used when the input clock fails. The PLL no longer tracks its input clock but uses the last valid frequency offset from memory (MEM). The proportional path is reset to zero and the integrator frozen at its last value. The
phase detector is reset to flush out its phase history.
i.e. switch is in position 2.
clock becomes an autonomous synchronization source In freerun mode or after entry into
holdover mode, frequency is subject to ageing drift and to the influence of temperature.
P. C.
MEM
VCO
CONTROLLER
L. F. | 1 | 
IN
OUT
2

## Slide 29: PLL MODES: HOLDOVER @ CONSTANT TEMPERATURE
Fractional frequency:
y(t)  y0  D  t
where y0  initial frequency offset
D  frequency drift rate (constant)
Time error:
0 0
x(t)  x  y  t  D  t 2
2
where x0  initial phase offset
y0  initial frequency offset
D  frequency drift rate (constant)
y(t)
t
D∙ t
y0
t
x0
x(t)
D t2
2
y0∙ t

## Slide 30: LOOKING AT NOISE

## Slide 31: PLL: JITTER & WANDER FILTERING
0
100
200
t [s]
xIN(t) [s]
xOUT(t) [s]
1 x 10 - 6
5 x 10 - 7
- 5 x 10 - 7
- 1 x 10 - 6
What is jitter/wander?
Jitter, wander, phase noise is a variation of the clock’s frequency/period/phase
Essentially a phase modulation (due to noise or other disturbances) of the carrier clock when compared to an ideal reference
  Jitter = short-term variations
  Wander = long-term variations
ITU-T G.810 defines noise frequencies <10Hz as wander and frequencies >10Hz as jitter
  In Telecom, the period of the clock is called Unit Interval (UI)
The function of a PLL is to attenuate jitter and transfer wander
In other words, tolerate noise at the input without losing lock to
the reference

## Slide 32: PLL: RESPONSE TO INJECTED NOISE
PLL is a low-pass filter for input noise
PD
LPF
DCO
Phase Noise (In)
Phase Noise (Out)
Oscillator
FL
Phase Noise (Out) Phase Noise (In)
PLL is a high-pass filter for oscillator noise
DCO
Phase Noise (Oscillator)
PD LPF
Phase Noise (Out)
Ref (In)
FH
Phase Noise (Out) Phase Noise (Osc)
20 log HOSC  j2f  [dB]
20 log H IN  j2f  [dB]
20 log HOSC  j2f  [dB]
20 log H IN  j2f  [dB]
OUT
X
xOUT t   xIN t  hIN t 
s   XIN s  HIN s 
where hIN t   impulse response
HIN s   transfer function  LaplacehIN t 
OUT OSC OSC
x
t   x t  h t 
XOUT s   XOSC s  HOSC s 
where hOSC t   impulse response
HOSC s   transfer function  LaplacehOSC t 

## Slide 33: PTP4L SW FILTER TEST RESULTS FOR G.8273.2
Page 33
# | Freq (Hz) | Ampl (ns) | Duration (s) | Pk-Pk Output (ns) | Gain (dB) | Upper Pk- Pk Limit (ns) | Lower Pk- Pk Limit (ns)
1 | 0.00391 | 200 | 1024 | 199.77 | -0.01 | 215 | 130
2 | 0.00781 | 200 | 896 | 200.11 | 0.00 | 215 | 130
3 | 0.01563 | 200 | 448 | 201.19 | 0.05 | 215 | 130
4 | 0.03125 | 200 | 224 | 205.06 | 0.22 | 215 | 130
5 | 0.06156 | 200 | 243.65 | 217.68 | 0.74 | 215 | -
6 | 0.12313 | 200 | 251.78 | 255.64 | 2.13 | 140 | -
7 | 0.24625 | 200 | 251.78 | 240.95 | 1.62 | 90 | -
8 | 0.4925 | 200 | 249.75 | 124.11 | -4.14 | 50 | -
09 | 0.985 | 200 | 249.75 | 58.95 | -10.61 | 35 | -
10 | 1.985 | 200 | 249.87 | 26.83 | -17.45 | 30 | -
Simple SW based Low Pass Filtering (BW = 0.4-0.5Hz), no PDV
Even if ptp4l settings adjusted for cut-off frequency (i.e. to be <0.1Hz), it will still be difficult to pass gain peaking (>2db!)

## Slide 34: DPLLS BECOMING COMPATIBLE WITH THE LINUX PTP HW CLOCK
Packet Switched Network
PHC
Infrastructure
SO_TIMESTAMPING
Socket Option
Protocol Stack
Kernel Driver
PTP
Master Clock
PTP timestamps PHC APIs
Kernel Driver
MAC
Hardware TSU
TOD
TSU
Servo
Linux PTP v4.0
Linux Kernel
User Space
PLL
(HW Servo)
Local Oscillator
Kernel Driver
TODPHC
Clock Signal
PPS
Drivers in Main Line Linux
Same APIs
Linux PTP supports PTP filtering in hardware timing chip to meet stringent ITU-T G.8273.2 Class D compliance (max|TE|L < 5ns,
gain peaking < 0.1dB)
Hardware filter is simpler to configure and use compared to software-based PI-filter included in ptp4l
Servo compliance becomes a mathematical certainty
Time is synchronized using the Linux PTP ts2phc application

## Slide 35: BENEFIT OF AN ADAPTIVE FILTER
Adaptive Filter

## Slide 36
PHASE LOCKED LOOPS (PLL)
CLOCK COMBINING

## Slide 37: COMBINING TWO PLLS
Phase Noise (Out2) Phase Noise (In2)
Phase Noise (Out2) Phase Noise (Osc2)
F2
Phase Noise (Out1) Phase Noise (In1)
Phase Noise (Out1)
Phase Noise (Osc1)
F1
PD
LPF
DCO
Phase Noise (In2)
Phase Noise (Out2)
Phase Noise (Osc2)
DCO
Phase Noise (Osc1)
PD LPF
Phase Noise (Out1)
Phase
Noise (In1)

## Slide 38: TWO PLLS: RESPONSE TO INJECTED NOISE
PD
LPF
DCO
PD
LPF
DCO
Phase Noise (Out)
Phase
Noise (In1)
Phase Noise (In2)
Phase Noise (Osc2)
F1 F2
Band-pass filter for In2 Noise to Out

## Slide 39: TWO PLLS: APPLICATIONS
Combiner
GNSS
receiver
Cesium clock
ePRTC
Output Line Interface
Input Line Interface
T-BC
Physical
Layer
Clock
PTP Slave Eingne
Time PTP Master
Clock Engine
PTP
PTP
PHY
PHY
GNSS & Cesium clock in enhanced Primary Reference Time Clocks (ePRTC)
GNSS & Miniature Atomic Clock
(MAC) in OCP-TAP Time Card
PTP & SyncE in boundary clocks (T-BC) and slave clocks (T-TSC)

## Slide 40: G.8273.2 T-BC: RESPONSE TO INJECTED SYNCE NOISE
A band-pass filter for SyncE Noise to PTP (Out)
Amplitude, dB
PD
1.2Hz
LPF
DCO
SyncE Noise (In)
SyncE (Out)
0.1Hz LPF
DCO
PTP (Out)
Time Stamp Unit (TSU)
PTP Stack
PTP
Network
offsetFromMaster
TCXO
T-BC1
PRTC
T-GM
T-BC2
T-BC9
End App.
Very little PDV
0.05 0.1
Frequency, Hz
1
10

## Slide 41: Timing is the heartbeat of the system