## Slide 1: Time Transfer and Ensembles Across Moving Platforms

## Slide 2: Outline
Precision Time and Frequency
  What is it? What are the needs and uses?
  GNSS are vulnerable
  Time Sync can help reduce over-dependence on GNSS
Principles of Time Transfer
  One-way vs Two-way time transfer
  Time transfer across moving platforms
  Relativistic effects
  PNTP
Time Scale Ensembles
  General principles, example algorithms
  Advantages and Challenges
  Distributed Ensembles
  Ensembles across moving platforms
Conclusions: Research Ǫuestions
How to optimally estimate delays among randomly moving platforms?
How to generate an ensemble time more stable than all member clocks even when they are very diverse?
Can ensembles of ensembles provide improved resilience and performance?
How best to account for clocks entering and leaving ensembles?

## Slide 3: Time and Frequency Sources
Frequency is fundamental. A clock produces a frequency by realizing principles of physics plus noise.
Time is an artifact. A time signal is produced from frequency by counting cycles. All clock times walk off from each other without bound.
UTC is the international reference. Local time can be steered to UTC.
3

## Slide 4: Comments about Time
Not the time that we directly experience as human beings
The time that we create as engineers and scientists.
  An artifact. We completely make it up
  The Time Standard (hours-minutes-seconds, year-months-days) is totally a human-created thing
  The labels we put on the 1-PPS pulse are arbitrary
  We count cycles of frequency in clocks
Our time standard is meant to approximate the “t” for time in our scientific equations. But that “t” is generally meant to be idealized: noise free and perfectly sequential

## Slide 5: Two Issues Here
Since a clock is a frequency device, the best clock possible exhibits only white noise on frequency, hence a random-walk in phase. Even the best clocks will walk off unboundedly in time.
Since the time standard is artificial, time MUST be transferred from the relevant time standard
  Transferring time requires
    A signal, providing the on-time pulse or a clock frequency
    Data, giving the date (hour-minute-second, year-month-day, etc)
Often what is needed is synchronization among locations, not UTC per se, though that is often the most efficient way to achieve sync

## Slide 6: Time Signal Plus Data
Time Distribution
Receiving Node
Async time msg: 05:00:00.000000 10/31/2014 Z
Physical On-Time Marker
After reception of Both, the receiver knows the time is
1. 05:00:00.000000
10/31/2014 Z, after receipt of the async data
2. Plus, xxx ns upon receipt
of on-time marker

## Slide 7: Time and Frequency Transfer: How to Deliver a Timing Reference
Time Transfer Accuracy Requires Calibrating Delays
  Imagine writing a letter: “It is now 2 PM– set your watch”
  Seal it in an envelope and drop it in a mail box
  Only useful if you know how long it took to get to you
  Now suppose you timestamped when you sealed the letter and the receiving person timestamped when he got it…
  And that you had accurate clocks!
Time Stability = Frequency Accuracy

## Slide 8: Some Current Applications that Need Precision Time
Enable New Knowledge
Agriculture
Defense
Smart Grid
Industrial Automation
Transportation and Connected Vehicles
Smart City
Source: Cisco (flavio@cisco.com)
Telecom

## Slide 9: Systems that Benefit from Precise Time
Telecom systems
  Multiplexing
  Packet networks
  Wireless access
  Optimal use of wireless spectrum
Broadcast services, such as Audio-visual transmission
Electric Power Grid
Data Centers
Financial Services
Location-based services
  1 ns = 1 foot
Cyber-Physical Systems (CPS)
  Local systems
  Global systems
Temporal determinism in software
Optimizes energy usage and resource allocation
Supports CPS timing (sensing to actuation)
Allows increased regulation in trades
Time stamping of events
  Correlation for analysis
  Data aggregation
Many, many more…

## Slide 10: One-Way Dissemination or Comparison System
Slide - 10
Clock 1
Clock 2
Clock 1 Systematics
and Noise
Clock 2 Systematics
and Noise
Delay, Perturbations, and
Measurement Noise
One-way Time Transfer requires determining and removing the Delay

## Slide 11: One-Way Time Transfer: GPS
Ephemeris error
Ionosphere
Troposphere
Satellite Vehicle (SV) Clock
Satellite signal is locked to the on-board atomic clock. Receiver can obtain time
and frequency of atomic clock from the RF signal.
50 Hz data channel gives the offset of:
Clock time from GPS time
the offset of GPS time from UTC
UTC
System Time

## Slide 12: Clock 2 locked to Clock 1
Slide - 12
Clock 1
Clock 2
Clock 1 Systematics and Noise
Clock 2 Systematics and Noise
Lock Loop Systematics and Noise: Contributions from
Measurement Noise and Path Perturbations

## Slide 13: GNSS-aided Time and Frequency Systems: Lock Local Oscillator to GNSS
Qz Osc.
Ǫuartz Crystal Oscillator
Tune
Compare
GNSS
GNSS
Rcvr
T/F System
Rb Vapor Phy Pkg
Qz Osc.
Rubidium Vapor
Atomic Oscillator
Tune
Compare
Output Time
and Freq.
GPS
Rcvr
T/F System
Or
Courtesy H. Fruehauf, ViaLogy LLC
Output Time aFnredqF. req.

## Slide 14: Two -Way Comparison System
Slide - 14
Clock 1
Clock 2
Clock 1 Systematics
and Noise
Clock 2 Systematics
and Noise
Two-way transfer depends on
the Path being Reciprocal:
d12 = d21
Measure t21= Clock2-Clock1
+d21
Measure t12= Clock1-Clock2
+d12

## Slide 15: Two-Way Time Transfer: Four Time Stamps
T4 09:00:025
T2 09:00:005
T3 09:00:015
Client
Server
T1 09:00:000
Time
Time
Corrected time 09:00:0225

## Slide 16: Security and Resilience
A lot of work has been done on cybersecurity, but security of timing is still developing
Since timing is both signal and data
  Security of data is like cybersecurity
  Security of timing signal is new to cybersecurity:
    does the signal come from the true source?
    has the signal been interfered with?
Resilience in time transfer generally means redundancy of systems
Time accuracy, UTC, most commonly comes from GNSS, which is vulnerable
to interference. Though one can have a direct connection to a source of UTC,
a national lab

## Slide 17: Spectra of GNSS Signals– Vulnerability
Slide 17
Primary Commercial Signal

## Slide 18: GNSS Vulnerability: Jamming
GNSS best feature and worst problem: it is extremely reliable
Jamming Power Required at GPS Antenna
  On order of a Picowatt (10-12 watt)
Many Jammer Models Exist
  Watt to MWatt Output – Worldwide Militaries
  Lower Power (<100 watts); “Hams” Can Make

## Slide 19: GNSS Vulnerability: Spoofing/Meaconing
Spoof – Counterfeit GNSS Signal
C/A Code Short and Well Known
Widely Available Signal Generators
Meaconing – Delay C Rebroadcast
Possible Effects
  Long Range Jamming
  Injection of Misleading PVT Information
No “Off-the-Shelf” Mitigation
Spoof Code GPS S.V. Code
Correlation %
100
Code Phase (t)
L P E
3. Pull Off
L P E
Code Phase (t)
Correlation %
100
2. Capture
Correlation %
100
Code Phase (t)
L P E
1. Match Real Code
Successful Spoof

## Slide 20: Time Without GNSS
Systems generally only need UTC for coordinating with distant systems, or with systems run by competitors
Generally, a system only needs time coordination across clocks participating in that system
Hence, time-transfer is critical
Alternate-PNT systems have been designed for self-consistent PNT

## Slide 21: Visual Summary: Stationary vs Dynamic clock ensembles
Can we use ensemble techniques to create an optimal dynamic network timescale?
21
?

## Slide 22: Remote clock synchronization
GPS is the best clock synchronization system ever built.
Time transfer is a method to synchronize two or more remote clocks to share the same time.
Clock synchronization is a means to maintain time across a network when an external reference like GPS is unavailable
Stationary clock ensembles have been used internationally in national labs to generate an improved reference time across global synchronized clocks, i.e. International Atomic Time (TAI) and Universal Coordinated Time (UTC)
Can we create a clock ensemble for dynamic platforms in a denied environment?
22

## Slide 23: Clock Synchronization
Architectures
Plesiochronous Strategy (Anarchy) Free-running (Current GPS
method each clock updated independently)
Master-Slave
Strategy (Despotism)
Links are continuous or periodic
Mutual Strategy (Democracy) Links are continuous or periodic Anyone can be the master
All can run an ensemble algorithm
M
M
Master-Slave
Strategy (Despotism)
M-S1,S6, S1-S2, S2-S3, S6- S5
This configuration has latency

## Slide 24: Time synchronization across a dynamic network
When GPS is denied we can establish a common time that is maintained across a stationary or dynamic network
For dynamic clocks motion correction is required due to relativity and to measure propagation delay :
  in a gravitational field clock rates are dependent on position and velocity and are different across the network
  propagation time asymmetries between platforms
For precision synchronization (nanosecond errors) between platforms the following measurements are required:
Time difference between clocks , 3-dimensional range, and relative velocity between platforms
A spatially distributed set of clocks, with rates adjusted to maintain synchronization, can create a coordinate time scale that is referenced to UTC

## Slide 25: Position, Navigation G Time Protocol (PNTP)
PNTP is a new network protocol for Two-Way Position Transfer
Extension of NTP / PTP to include Position, Velocity, Acceleration (PVA)
  Time Distribution => Position Distribution
    Terminology: Server/Client => Reference/Asset
    Hierarchical Network: Stratum 1 Server => Primary Reference
Explicitly handles time G position distribution for moving References and Assets
  Time of Arrival (TOA) and Time Difference of Arrival (TDOA) positioning
  Kalman Filtering methods for PVA tracking and prediction
  Compensation for Special and General Relativity (velocity, gravity)
Luminous Cyber Corp (Barry, Weiss), initial development funded by USAF SBIR
  First flight by UAS in GPS-denied airspace April 2024
Looking to collaborate to bring PNTP to IETF, IEEE
  Related efforts NTPv5, IEEE CSPTP (Client Server PTP)

## Slide 26: Position, Navigation G Time Protocol (PNTP)
Reference
Asset
(a) NTP (Stationary)
(b) PNTP (Stationary)
(c) PNTP (Moving Asset) (d) PNTP (Moving Reference, Asset)
t1 t4 t1,p1,v1,a1 t4,p4,v4,a4 t1,p1,v1,a1 t4,p4,v4,a4 t1,p1,v1,a1
t4,p4,v4,a4
t2 t3 |  | t2,p2,v2,a | t3,p3,v3,a |  | t2,p2,v2,a | t3,p3,v3,a | t2,p2,v2,a | t3,p3,v3,a
 |  | 2 | 3 |  | 2 | 3 | 2 | 3
Enables Spherical (TOA) and Hyperbolic (TDOA) positioning
Help support Kalman Filtering methods for PVA tracking and prediction
Can provide Compensation for Special and General Relativity
Accuracy is improved for packet rates >= 10/s
3+/4+ TOA/TDOA References
Spherical (TOA) Positioning: Hyperbolic (TDOA) Positioning:
3D Asset Position is at intersection of spheres 3D Asset Position is at intersection of hyperboloids

## Slide 27: Position, Navigation G Time Protocol (PNTP)
LEO
Satellite
Reference Receiver
Drone/UAV
UWB LPI/D RF
Links
Hierarchical
Stratum 1 Primary References
Stratum 2 Assets/References
Stratum 3 Asset
ROV RF

## Slide 28: What is a Time Scale Ensemble?
Inputs:
  The statistical characteristics of each member
  Measurements of times or frequencies of all members with respect to a reference clock
  N-clocks produce N-1 independent inputs
Outputs:
  Ensemble time offset from each clock, thus N outputs
    N-1 inputs and N outputs requires an additional equation, such as optimizing stability
  Physical realization of ensemble time
Advantages:
  Minimize single points of failure
  Output does not depend on a single device
  Ensemble provides error detection
  Theoretically the output is better than all contributors— and there are opportunities for improvement

## Slide 29: Steered clock
Data from clock ensemble
Phase Stepper generates Scale as Offset from Clock
Measurement system and time scale computation | 
 | Steering Control
Steered output
Clocks are not
steered

## Slide 30: Dynamic clock ensemble concept
Assumes correction of dynamic delays as well relativistic effects
Each platform clock measures and corrects its offset to ensemble time
Each platform produces the same ensemble time using the algorithm
Similar to the generation of TAI/UTC but in a dynamic environment
Analysis shows that ensembles can be successfully used on moving platforms, and there are research opportunities
  Realizing the ensemble will have short-term issues due to latency in delivering the time epoch for steering
  Relative Position Error between platforms translates to a measurement error, which degrades the stability of the ensemble
  With highly dissimilar clocks, there are research opportunities to output the best of every clock
30

## Slide 31: How clocks behave in space – relativity and environmental fluctuations
Initial approach for GPS: Relativistic corrections were made on board, clocks ran fast
Now GPS clocks are designed to run slow on the surface so in orbit they run at the correct rate
Goal is to have clocks behave as if they are in the laboratory but:
  Satellites do not have a constant velocity:
    Tidal forces (Sun and moon)
    Eccentricity
    Earth is not a perfect sphere, oblate
    Solar wind and some atmospheric drag in low LEO
  Fluctuations of the satellite environment
    Thermal (in and out of sunlight)
    Magnetic fields ( on board currents, earth’s field)
    Vibrations and mechanical stability
Time transfer mitigates the need for long term stability
31

## Slide 32: Satellite constellation synchronization: conceptual approach
Correct for clock relativistic effects
  Transformation from proper time to coordinate time on each satellite (Can be done by design for circular orbits)
Transfer coordinate time and correct for propagation path asymmetry (multi-exchange TWTT protocol)
  3 transmissions required by each platform to correct for motion and share measurements
Timeline in orbital plane at 7000 km above the Geoid
  77 ms between platforms
At 7000 km altitude:
  Chord length =23,171km
  Platform moves 421 m during signal propagation nearly in a straight line.
    Have communication link already established prior to conducting TWTT

## Slide 33: Next steps in feasibility of dynamic ensembles
In laboratory ensembles the time comparison measurements occur at the same epoch
  There is no latency when clock N is compared to clock M
  Develop a quantitative analysis of airborne dynamics where the relative motion between platforms is random
Currently we require that the propagation delays and the path asymmetries are measured.
  What is the behavior of the ensemble if the clocks in the network are compared at different epochs (measurement times)?
Conduct a simulation comparing Time Scale Algorithms and > 5 airborne platforms that includes:
  Propagation effects, latencies, with varying ranges and range rates
  Use 3+ diverse types of clocks
  Time scale stability and how to handle the addition and subtraction of platforms
  Include the effects of measurement noise
33

## Slide 34: Research Ǫuestions
How do we optimally estimate delays among randomly moving networks of clocks?
  Multiple two-way time transfer (TTT) measurements are needed, but what is optimal?
  How do we share TTT results across the network in a timely manner
  Can we optimize the PNTP structure to account for all delays and relativistic effects, thus minimizing needed measurements?

## Slide 35: Research Ǫuestions
How do we generate an ensemble time that is more stable than all clocks, even when the statistics of the clocks are very different?
  This has been demonstrated when clocks are similar: e.g. all Rb clocks
  Can we similarly optimize performance if we have clocks as different as a Ǫuartz LO and a GNSS receiver
    Ǫuartz LO has very good short-term, but poor long-term stability
    GNSS receiver has relatively poor short term, but very good long term
    Typically, we lock an LO to GNSS to obtain the best short-term and long-term
    Can we have many diverse clocks and get optimal performance of the ensemble?

## Slide 36: Research Ǫuestions
How do we optimize performance of a distributed ensemble with clocks on moving platforms?
  For satellites in orbit, the latency can be large. For LEO satellites ~ 10’s of ms. For MEO to GEO satellites perhaps 0.1 s.
  Can we optimize the filtering of range errors by the ensemble?

## Slide 37: Research Ǫuestions
4. Ensembles of ensembles– can these provide improved
resilience and performance, for example, in Cyber-Physical
Systems?
In uncertain measurement environments
  Autonomous vehicles
  Moving platforms
  Battlefield environments
Synchronization Islands
  GPS denied environments
  e.g. urban canyons
  clusters of drones, aircraft, boats, soldiers
Assuming better sync accuracy and reliability in islands, worse in the
ensemble of ensembles

## Slide 38: Research Ǫuestions
Clocks entering and leaving ensembles
  Estimating Clock Stats
    In uncertain environments clock stats must be estimated adaptively
    Short term behavior can be converged on relatively quickly
    Long-term behavior takes a long time to learn accurately– determines long-term behavior of ensemble
    A high-weight clock leaving unexpectedly can disrupt the ensemble time and frequency

## Slide 39: Research Ǫuestions
Clocks entering and leaving ensembles
  Disruption of the Ensemble
    Short term behavior can be converged on relatively quickly
    Long-term behavior takes a long time to learn accurately– determines long-term behavior of ensemble
    A high-weight clock leaving unexpectedly can disrupt the ensemble time and frequency

## Slide 40: Conclusions
Time transfer across moving platforms requires more research
  Optimally determine changing delays– cannot assume symmetric!
  Minimize needed TTT measurements
  Communicate PNTP data to all members
Distributed Time Scale Ensembles Across moving Platforms
  Advantages
    Optimize predictability
    Improve resilience
  Optimizing an algorithm for highly varied clocks on moving platforms in
uncertain environments
Needs more research– Can expand on previous work
Has conflicting requirements
We would like collaborators!