# PCB General data.
- Panel Dimension: 439,06 mm x 233,30mm
- PCB Dimension: 439,06 mm x 219,20mm
- Thickness: 1,54 mm ± 10%
- Material: FR4 High Tg
- Number of layers: 6
  - 4 routing layers (“Top Layer” , “Mid-Layer1”, “Mid-Layer-2” and “Bottom Layer”)
  - 2 plane layers (“GND” and “PWR”)
- Components total: 518 (top: 192, bottom: 326)
- SMD components: Yes, both sides
- Silkscreen: Yes, both sides
- Nets: 472
- Vias: 1347
  - Hole Size: 0,3 mm
  - Via Diameter: 0,7 mm
- Pads: 2418
- Plating Finish: Nickel-Gold
- Lead-Free Components: Yes
- Controlled Impedance: Yes, on “Top Layer”, “Mid-Lyer1”, “Mid-Layer-2” and “Bottom Layer”

# Stack-Up Diagram

Top Layer				55 µm
PrePreg				214 µm
Mid-Layer1				17 µm
Core				360 µm
GND				17 µm
PrePreg				220 µm
PWR				17 µm
Core				360 µm
Mid-Layer1				17 µm
PrePreg				214 µm
Bottom Layer				55 µm
Thickness Total:				1,54 mm ± 10%

# Layer Stack-Up Detail
Layer / Name	Gerber / Document	Copper / Thickness	Dielectric / Height	Dielectric / Material	Dielectric / Constant	50Ώ Impedance Width	100Ώ Differential Impedance Width/Gap
Top / Solder Mask	(.GTS)		0,010mm	Solder Resist	3,5
Top Layer	(.GTL)	0,055mm				0,350mm	0,25mm/0,15mm
PrePreg			0,214mm	FR-4	3,8
Mid-Layer1	(.G1)	0,017mm				0,18mm	0,18mm/0,22mm
Core			0,360mm	FR-4	4,7
GND	(.GP1)	0,017mm
PrePreg			0,220mm	FR-4	3,8
PWR	(.GP2)	0,017mm
Core			0,360mm	FR-4	4,7
Mid-Layer2	(.G2)	0,017mm				0,18mm	0,18mm/0,22mm
PrePreg			0,214mm	FR-4	3,8
Bottom Layer	(.GBL)	0,055mm				0,350mm	0,25mm/0,15mm
Bottom / Solder Mask	(.GBS)		0,010mm	Solder Resist	3,5