## Slide 1: Преимущества точного времени для дата-центров
9
Coherency (Согласованность)
Ensure that the data are the 
same on distributed devices
Reduce the number of data 
replicas
Allow coordinate actions  starting at same time increase the probability to finish at the same time
Efficiency (Эффективность)
Reduce the hysteresis (ε uncertainty bound)
Pre-schedule tasks to handle known low latencies
Pipelined assignments to improve efficiency
Visibility
(Прозрачность)
Have a clear view of the real order of events
Measure latency to control bottlenecks
Carefully allocated resources to avoid any problems

## Slide 2: ВНЕДРЕНИЕ ВЫСОКОЙ ТОЧНОСТИ В ПРИЛОЖЕНИЯ
Processor instructions |  | 
RDTSC | TPAUSE | …
Always Running Timer  TSC (CPU Timer Core)
PCIe Bus PTM (Precision Timing Measurement)
PTP OC Follower (OCXO on PCIe Node > PPS out)
Timing Distribution
WR (HATI)
PTP TC (1 to 5 hops)
Sundial, etc…
GNSS Timing Reference
PRTC-A | PRTC-B | ePRTC-A | …
Точная синхронизация времени на уровне PCIe

## Slide 3: Сокращение абсолютного временного (1,5 мкс)
Повышение точности распределения времени позволяет увеличить времx автономной работы (holdover) и, следовательно, повысить устойчивость системы.

## Slide 4: Относительный и абсолютный временной запас
Новое приложение: Вводятся в эксплуатацию новые приложения, требующие очень точной синхронизации времени для межсерверного анализа.
Требования: Приложение требует, чтобы все серверы в рамках одного регионального дата-центра выполняли определенные операции с точностью до 600 наносекунд.
Проблема с PTP: Существующая система синхронизации времени по протоколу PTP (PTP) имеет внутреннюю ошибку времени (ε) в 100 наносекунд (обозначается как PRTC-A). Это значит, что время на серверах в одном регионе может отличаться на 100 нc.
Решение с помощью WR: Технология WR позволяет распространять один и тот же эталонный часовой сигнал по всему региональному дата-центру.
Преимущества Qantum-PCI WR:
Устранение ошибки PRTC-A: Поскольку все серверы будут синхронизированы по WR, внутренняя ошибка PTP (PRTC-A) устраняется, и все серверы будут синхронизированы с точностью до 600 нc.
Увеличение времени автономной работы (holdover): В случае помех или сбоя GNSS сигнала, WR будет использовать встроенные атомные часы для обеспечения точного времени в режиме автономной работы. Благодаря устранению ошибки PRTC-A, время автономной работы не будет расходоваться на компенсацию этой ошибки.

## Slide 5: EQUIVALENT TO 3GPP REQUIREMENTS
Tech / Application | Time-error | 
RU-GMC (DU-GMC) | ±1.5 µsec (±1.1 µsec) | Absolute
Intra-band non-contiguous CA | ±130 nsec | Relative
Inter-band CA | ±130 nsec | Relative
Coordinated Multi-Point (CoMP) | ±130 nsec | Relative
Intra-band contiguous Carrier Aggregation (CA) | ±65 nsec | Relative
MIMO / Transmit Diversity (Cat A+) | ±32 nsec | Relative
High-Accuracy Positioning Services (same DU) | ±10 nsec | Relative
Self-driving / Autonomous car | < 5 nsec | Relative
Tech / Application | Time-error (ε) |  | 
PTP DC Profile Timing distribution | ±2.5 µsec | Absolute | -
… | … | … | 
Coherent Database with low epsilon | ±100’s nsec[*] | Absolute | SW
… | … | … | 
Desagrated hardware (GPU, FPGA, DPU, etc..) | < ±100 nsec[*] | Relative | HW
Cross device events analysis for debugging | ±10’s nsec[*] | Relative | HW
High Frequency Trading Coordinate Action | ±10’s nsec[*] | Absolute | HW
High Frequency Trading Visibility Network | < ±1 nsec | Relative | HW
DC community (Qantum-PCI) needs to agree on a set of requirements for each application/technologies:
Not only based on how well timing distribution performs
But answering what is the “theorical and meaningful” limit for a specific application
[*]: The provided value are to be defined and just provided as example to illustrate that more specific requirements are needed by the industry.
Telecom requirements (3GPP)
Datacenter requirements (???)

## Slide 6: REFERENCE ARCHITECURES
1. Cisco 3-levels leaf/spine
2. Meta DC-Fabric (F16)
1 building
16 superspines
64 pods  48 x racks/pod
~140K server/DC
1 Region  6 buildings (F16)
16 fabric planes
48 pods  48 x racks/pod
~100K servers/DC  ~600K servers/region

## Slide 7: Слои синхронизации времени в дата-центрах
TL0 | TL1 | TL2 | TL3 | TL4
Intercity DC | Regional Area | Building Area | Pod Area | Rack Cabinet
>100km N+1 devices (N network hops) | <100km (metro) ~1-6 buildings | <10km ~64 pods | <100m ~48 racks | <10m ~40-48 servers
GNSS comparison “results from NY- Chicago tests” | DWDM channels Main GM (with Atomic Clock) | Dedicated fiber Backup GM with GNSS Antenna | Dedicated fiber High Port Density | Fiber (HATI/PTP) Coaxial (PPS) Copper (PTP)

## Slide 8: UC-A: REFERENCE ARCH FOR DC PROFILE
GM
TC
GM
GM
GM
TC
TC
TC
TC
TC
…
…
…
… …
… …
TC
TC
TC
… …
…
TC | 
OC | 
OC | 
 | …
OC | 
TC | 
OC | 
OC | 
… | 
OC | 
TC
TC | 
OC | 
OC | 
… | 
OC | 
TC
TC | 
OC | 
OC | 
… | 
OC | 
…
…
…
TC | 
OC | 
OC | 
… | 
OC | 
Few Open Time Servers (GM) at the top of the DC to discipline all nodes
↓
Very Simple solution to put in place
Cost effective solution
No vendors lock-in
PTP Timing distribution ≈1us
Not scalable for hyperscale
>100’000 server  Open Time Servers CPU can not support
this load
8

## Slide 9: UC-B: REFERENCE POD ARCH FOR DC PROFILE
4x Open Time Servers (GM) per pods
↓
Simple solution to put in place
Reduce the number of hops
No vendors lock-in
GM handles between 5-15K clients
PTP Timing distribution ≈400ns
Many GNSS receivers to handle
Complex RF installation: Splitter, Amplifiers
Many references can diverge ±100ns + calibration issues
GM
Super spine
Super
spine
TC
TC
TC
TC
…
…
…
… …
… …
TC
TC
TC
… …
…
TC | 
OC | 
OC | 
… | 
OC | 
TC | 
OC | 
OC … | 
OC | 
TC
TC | 
OC | 
OC | 
… | 
OC | 
TC
TC | 
OC | 
OC | 
… | 
OC | 
…
…
…
TC | 
OC | 
OC | 
… | 
OC | 
GM
GM
GM
GM
GM
GM
GM
9

## Slide 10: ART+NIC SOLUTIONS
UC-A: ART @ Top of DC
UC-B: ART @ Top of Pod
Distribution
Layer
Reference Layer
Client Layer
S pi ne 48 ports
1U RACK SERVER
TOR 48 ports
OPEN
TIME SERVER
ART ART GNS
NIC
40 G/1 00G
Distribution
Layer
Reference Layer
Client Layer
S p i ne 48 ports
1U RACK SERVER
TOR 48 ports
Qantum TIME SERVER
ART ART GNS
NIC
40 G/1 00G
192
por ts
switch
For 64xpods/DC with at least 4xOpenTimerServer
 256 GNSS antennas through DC
21

## Slide 11: UC-C: WR TO THE TIME SERVER
22
Using WR at the core of DC to synchronize all PTP GM master (Open
Time Server)
↓
Simple solution to put in place
Reduce the number of hops
GM handles between 5-15K clients
Sharing a common clock (<1ns accuracy)
Linked clocks increase resiliency and accuracy
Solution for intra-DC and inter-DC
Only 1 or 2 GNSS receivers to install
PTP Timing distribution ≈400ns
Relative accuracy is reduced by ±100ns
GM
Super spine
Super
spine
TC
TC
TC
TC
…
…
…
… …
… …
TC
TC
TC
… …
…
TC | 
OC | 
OC | 
 | …
OC | 
TC | 
OC | 
OC … | 
OC | 
TC
TC
OC
OC
OC
…
TC
TC
OC
OC
OC
…
…
…
…
TC | 
OC | 
OC | 
… | 
OC | 
GM
GM GM
GM
GM
GM
GM
GNSS
GNSS
WR

## Slide 12: INTER DC TRIANGLES
DC #C
DC #A
DC #B
Secure Sync
2400
GNSS
WR-Z16
IN OUT
1PPS10M Hz 1PPS10M Hz
GMa
Secure Sync 2400
GNSS
IN
OUT
1PPS10M Hz 1PPS10M Hz
W
R-Z 16
GMb
Secure Sync
2400
GNSS
1PPS10M Hz 1PPS10M Hz
WR-Z16
IN OUT
GMc
DWDM (40km)
DWDM (60km)
PTP OC Client Layer
PTP
Lower Timing Distribution Layer
WR
Upper Timing Distribution Layer
PTP OC Client Layer
WR
Upper Timing Distribution Layer
PTP
Lower Timing Distribution Layer
DWDM (25km)
PTP OC Client Layer
PTP
Lower Timing Distribution Layer
WR
Upper Timing Distribution Layer
WR-Z16
IN OUT
1PPS10M Hz 1PPS10M Hz
DUT
A resilient solution by design with a
OCP-TAP: WR in datacenters
triangle between 3xDC in the same
regional area (metro-area)
↓
DC#A has by default the main/active GMa
The GMb & GMc only monitor their GNSS offset in respect to WR from GMa
The link betweem GMb-GMc is in survey mode (only used to compute offset)
DUT has been placed below GMa but could be placed anywhere.

## Slide 13: INTER DC TRIANGLES (FAILURE)
If a spoofing attack is executed on GMa
the linked-triangle will detect abnormal
behavior and select a new GW
↓
A simple voting mechanism between at least 3 participants is always run-in background
The majority should not drift away from the mTIE>100ns
(PRTC-a)
When drift is detected on GMa it will stop being the active GM and enter HO mode
Meanwhile the next valid timing source GMb become the active GM
The GMa & GMc become slave of the GMb but continue monitoring their GNSS offset
The DUT smoothly transition from GMa to GMb
DC #C
DC #A
DC #B
Secure Sy nc
2400
GNSS
WR-Z16
IN OUT
1PPS10M Hz 1PPS10M Hz
GMa
Secure Sy nc 2400
GNSS
1PPS10M Hz 1PPS10M Hz
IN OU
W
R-Z 16
T
GMb
Secure Sy nc 2400
GNSS
1PPS10M Hz 1PPS10M Hz
IN OUT
WR-Z16
GMc
DWDM (40km)
DWDM (60km)
PTP OC Client Layer
PTP
Lower Timing Distribution Layer
WR
Upper Timing Distribution Layer
PTP OC Client Layer
WR
Upper Timing Distribution Layer
PTP
Lower Timing Distribution Layer
DWDM (25km)
PTP OC Client Layer
PTP
Lower Timing Distribution Layer
WR
Upper Timing Distribution Layer
WR-Z16
IN OUT
1PPS10M Hz 1PPS10M Hz
DUT

## Slide 14: EXAMPLE: FAILOVER WITH DRIFT DETECTION @ GMA
External lab measurement
View from the monitoring framework

## Slide 15: C: WR TO THE TIME SERVER
C1: Through PPS cable
C2: Through HATI NIC
Distribution Down Layer
Distribution
Up Layer
Reference
Layer
Client
Layer
S pi ne 48 ports
TIME SERVER
40 /100 G
1U RACK SERVER
S ecure Sy nc 2 400
GNSS
IN OUT
1PPS10M Hz 1PPS10M Hz
WR-Z 16
TOR 48 ports
WR-Z EN TP-FL
OUT IN
10M SI NCLKTTL 1PS 1PS 1M0Hz
FPO 8x
Distribution
Down Layer
Distribution
Up Layer
Reference
Layer
Client Layer
Spine 48 ports
TIME SERVER
1U RACK SERVER
SecureSync 2400
GNSS
1PPS10M H1zPPS10MHz
IN O UT
WR-Z16
TOR 48 ports
QSFP+ QSFP+ Sm ar t NI C
Any 40G/100G NIC cards with PPS input can works
Adding extra WR-TPFL device with FPO to provide up
to 8xPPS (4xPPS/4x10MHz)
HATI can forward clock information (TAI, Class, Accuracy, Leapsec, …) from GNSS to the Time Server
Ongoing Solution…

## Slide 16: HATI-SMARTNIC
HATI is an IP-core embedded in FPGA
At least 1x10G link is reserved for WR
  For Redundancy: HARTI can be used and will consume 2x10G links.
1PPS/Clk/ToD are forwarded to the
user IP-cores
Local oscillator of smartNIC can be disciplined with sub-ns accuracy (through WR-HATI)
Outgoing PTP packets are timestamps with sub-ns accuracy (from HATI-WR)
Time Server (CPU)
SmartNIC
FPGA (Xilinx)
HA(R)TI IP-CORE
QSFP
User Endpoints IP-Cores
WR timing network
1PPS
ToD
CLK
Mgt*
PCIe
QSFP
GTx
GTx
GTx
GTx
Crossbar
User IP-Cores
GTx
GTx
GTx
GTx
PTP data network
10G
40G
10G
Timing User IP-Cores
SMA
1PPS
vcxo
PTP daemon (GM)

## Slide 17: HATI – NATIVE WHITE RABBIT SUPPORT
HATI is being integrated with Arista, Cisco and LDA Technologies L1-switches.
High Accuracy timing integration in Xilinx FPGAs (including US+).
Sub-nanosecond time accuracy on NICs can be achieved leveraging this technology.
No need for expensive oscillators/clocks or dedicated hardware.
Distribution over fiber without calibration. Remove the need for coaxial cables.

## Slide 18
UC-D: WR UNTIL TOR
Timing network and data network are independent until TOR that works as PTP BC
↓
Integration of HATI into TOR FPGA
Accuracy @ TOR BC  <1ns
Few PTP clients (<50) for TOR BC Only 1 hops PTP
Accuracy @ OC Server  10’s ns
Resilient solution
OC NIC can be very basic
Adding a parallel timing network
Super spine
Super spine
Spine
Spine
Spine
Spine
…
…
…
… …
… …
Leaf
Leaf
HATI-WR
BC TOR
Leaf
… …
HATI-WR BC TOR
HATI-WR BC TOR
…
OC
OC
OC
OC
OC
OC
…
HATI-WR BC TOR | 
OC | 
OC | 
… | 
OC | 
HATI-WR BC TOR | 
OC | 
OC | 
… | 
OC | 
… Leaf
Leaf …
OC
OC
… …
OC
WR
WR
…
… …
…
WR
GNSS
GNSS
WR WR
WR
WR
WR
WR WR
WR WR
WR
…
18

## Slide 19: UC-D: WR UNTIL TOR
Timing network and data network
are independent only TOR
↓
Integration of HATI into TOR FPGA
Accuracy @ TOR BC  <1ns
Few PTP clients (<50) for TOR BC Only 1 hops PTP
Accuracy @ OC Server  10’s ns
Resilient solution
Adding a parallel timing network
Client Layer
Distribution
Layer
Data only
Reference
Layer
S pi ne 48 ports
1U RACK SERVER
S ecure Sync 2400
GNSS
IN OUT
1PPS10M Hz 1PPS10M Hz
WR
-Z 16
192
por ts switch
WR-Z 16
IN OUT
1PPS10M Hz 1PPS10M Hz
WR-Z 16
IN OUT
1PPS10M Hz 1PPS10M Hz
HA TI-TOR 48 ports
19

## Slide 20: RECAP: TIME BUDGET OPTIMIZATION
20
Improving accuracy for timing distribution allows to increase holdover budget and thus to enhance resiliency
Through WR a common clock is shared among the DC and thus it allows to:
  Remove PTRC-A time-error.
  Dedicate Holdover budget to final OC node

## Slide 21: UC-A/B: DETECTION OF ROGUE TC
GM
TC
GM
GM
GM
TC
TC
TC
TC
TC
…
…
…
… …
… …
TC
TC
TC
… …
…
TC | 
OC | 
OC | 
… | 
OC | 
TC | 
OC | 
OC | 
… | 
OC | 
TC
TC | 
OC | 
OC | 
… | 
OC | 
TC
TC | 
OC | 
OC | 
… | 
OC | 
…
…
…
TC | 
OC | 
OC | 
… | 
OC | 
Internal cross-check to ensure linearization must be used to detect Rogue TC
33
Checking only OC in the same rack might result in OK value.
Need to find where the results start to diverge
Consuming network bandwidth and CPU cycles for timing checking

## Slide 22: UC-E: SURVEY WITH WR SUPPORT
Add few strategically placed WR devices to act as ground-truth for PTP OC clients.
↓
Ground-truth devices are disciplined by WR with sub-ns accuracy
Mainly used as monitoring device by measuring PTP communication from OC
GM
TC
GM
GM
GM
TC
TC
TC
TC
TC
…
… …
… …
TC
TC
TC
TC
… …
TC
TC
…
OC
OC
OC
OC
OC
OC
…
TC
TC | 
OC | 
OC | 
 | …
OC | 
TC
TC
OC
OC
…
…
…
OC
OC
OC
… …
WR
WR
…WR
WR …
WR
WR
…
OC … …
…
WR
…
22

## Slide 23: UC-F: WR как эталон точного времени
Insert some probes in small percent of servers (ideally 1/rack)
↓
Ground-truth devices are disciplined by WR with sub-ns accuracy
Only used as monitoring device by measuring PTP communication from OC (1-hop TC)
Can be used as PTP ground-truth master to enhance any cross- exchange PTP solution (i.e., SquarePTP).
GM
TC
GM
GM
GM
TC
TC
TC
TC
TC
…
… …
… …
TC
TC
TC
… …
TC
…
TC
TC
OC
OC
…
TC
TC
OC
…
…
…
OC
OC
…
…WR
WR …
…
OC … …
…
WR
…
TC | 
OC | 
OC | 
 | …
OC +WR | 
OC
+WR
TC | 
OC | 
OC | 
… | 
OC +WR | 
OC
+WR
OC
+WR
WR
WR
WR
WR
23

## Slide 24: RESUMING USE-CASES
UC-A: Open Time Server above super-spine
  Simple to install but can not handle hyperscale DC numbers (>10K clients)
UC-B: Open Time Server per pods
  Complex RF installation with calibration issue
UC-C1: WR at core providing PPS to the GM
  Common clock shared across intra/inter-DC: needs extra TPFL-FPO device, no clock information forward to PTP GM.
UC-C2: WR at core providing PPS to a HATI compatible smartNIC
  Common clock shared across intra/inter-DC: needs smartNIC HATI compatible.
UC-D: WR timing until TOR device
  All TOR share the same clock, 10’ns accuracy at OC with only 1-hop PTP. A parallel timing network is needed.
UC-E: PTP Survey using scattered WR-Z16 devices
  Few strategically placed WR devices needed per pod to measure PTP offset. Can only be used to measure quality of link.
UC-F: Some ground truth server with PTP+WR (using HATI-NIC)
  Ideally 1 PTP-HATI NIC per rack to provide ground-truth allowing to enhance other protocols

## Slide 25
Создание основы для
будущих высокоточных приложений.
Создание более надежных
и устойчивых систем.
Увеличение времени
работы в автономном режиме (holdover).
Повышение точности
синхронизации времени.
Преимущества использования Qantum-PCI