## Slide 1: SyncESMC
Реализация многотактового ESMC ITU-T G.781
©2024 ShiwaNetwork | www.snet |

## Slide 2: Dd Введение
SyncMonk is an early stage bootstrapped startup founded in 2020. We are based in Bangalore, India with main focus on time synchronization services and products. SyncMonk provides complete integration services to Telecom, Networking and Semiconductor companies.
SyncMonk believes in innovating things and is working on the Time Services portfolio including software and hardware solutions.
Solutions offered by SyncMonk are:
  SyncESMC v1.0 an ESMC implementation based on ITU-T standard,
  FishEye - Set your Vision Clock Monitoring tool for sync and time services
  SyncPTP ptp stack optimized and in compliance with IEEE 1588-2019 standard and respective profiles.
www.syncmonk.net| info@syncmonk.net

## Slide 3: Agenda
Overview
Why SyncESMC
Architecture
  Design GOALS
  Configuration
  Packet Engine
  ESMC State Machine
  Hardware Abstraction Layer (HAL)
External Interface
FishEye
Demo Video
www.syncmonk.net| info@syncmonk.net

## Slide 4: Обзор
ESMC — это логический канал, который передает информацию SSM.
Информация SSM определяет уровень качества EEC.
Он основан на ITU-T G.8264 (03/2018) и ITU-T G.781 (04/2020).
Ethernet SSM — это медленный протокол Ethernet, определенный ITU-T.
www.syncmonk.net| info@syncmonk.net

## Slide 5: Топология сети синхронизации
www.syncmonk.net| info@syncmonk.net

## Slide 6: Почему SyncESMC
Аппаратный абстрагированный стек ESMC.
Соответствует G.781 (04.2020) и G.8264 (03.2018).
Упрощенная однопоточная архитектура.
Взаимодействие со стеком PTP (для поддержки IWF)
Поддержка динамической конфигурации.
Мониторинг с помощью FishEye
Поддержка Intel® E810XXVDA4T, Renesas® ClockMatrix™ 8A34001 и AuraSemi® 5508 PHC.
www.syncmonk.net| info@syncmonk.net

## Slide 7: Архитектура

## Slide 8: ЦЕЛИ дизайна
Однопоточная архитектура.
Поддержка нескольких аппаратных средств с использованием HAL
Поддержка нескольких часов
Внешний мультиплексор для входных сигналов
Футуристический дизайн для поддержки драйверов ядра с минимальными изменениями.
Взаимодействие со стеками PTP от разных производителей.
Встроенная поддержка конфигурации и мониторинга сети.
Микросервис, совместимый с SONiC
www.syncmonk.net| info@syncmonk.net

## Slide 9: Конфигурация
Модуль конфигурации имеет два режима:
Режим статической конфигурации
  Файл конфигурации на основе JSON.
  Система загружается с предопределенной конфигурацией
  Конфигурация в основном подразделяется на
    Устройство
    Порт
    Мониторниг
Динамическая конфигурация
  REST API
  Модель Netconf-yang для O-RAN
www.syncmonk.net| info@syncmonk.net

## Slide 10: Пакетный механизм
Packet Engine участвует в деятельности, связанной с интерфейсом.
Пакетный прием
Пакетная передача
События соединения порта/соединения
(сетевого соединения)
Фильтрация пакетов
Различные типы сокетов и типы интерфейсов.
Разделяется с помощью библиотеки пакетного
механизма.Raw Socket
UDS Socket
APIs
Packet Filter
RX
TX
Application
RTNL
Link
Events
www.syncmonk.net| info@syncmonk.net

## Slide 11: ESMC State Machine
Core of the ESMC stack.
Interacts with the Packet Engine, Configuration Engine, HAL
Decides to select the source port based on the Best Port Selection Algorithm. (Quality, Priority, Hops)
Handles the timer interrupts for Time outs for Hold off time, no activity on the port, Holdover timeout and Restore timers.
Interacts with HAL to configure the Hardware.
ESMC
State Machine
Packet Engine
Configuration
Timer
HAL
1
2
3
4
5
Packet Engine updates the packet metadata to Database.
Configuration can be updated run time
Timer-based events for TX packets, Holdover events, and RX timeout events.
Hardware events like LOS, OOF, PLL Loss
PLL ID and PLL input selection instructions to HAL.
www.syncmonk.net| info@syncmonk.net

## Slide 12: External MUX for Input Signals
Supports Multiplexing, where it can be configured for the maximum number of Sources available for a PLL and the maximum number of inputs which can be given to the PLL.
Runs an algorithm to select the best ports and based on priority programs the MUX.
Works with any of the available hardware where the number of inputs to PLL is more than the number of sources available. For e.g Broadcom XGS chips for Data Center switches
www.syncmonk.net| info@syncmonk.net
PLL
MUX
Source
Inputs

## Slide 13: Hardware Abstraction Layer
Hardware Abstraction Layer.
Hardware vendors can plugin their HAL functions to integrate with SyncESMC.
Ready for Kernel exposed APIs (in future) for controlling the hardware.
Hardware interrupt and status monitoring.
Multiple vendors’ PLLs can be controlled by the same stack.
HAL
(Hardware Abstraction Layer)
www.syncmonk.net| info@syncmonk.net

## Slide 14: External Interface
UDS socket can be used to interact with external applications
  PTP stack
    Seamless integration with any PTP stack over a UDS socket.
    SyncESMC can convert Clock Class to Clock quality as per G.8275.2 Annex F.
External Application Interfaces
  FishEye
  Configurations
www.syncmonk.net| info@syncmonk.net
SyncESMC
UDS
PTP
Exchange information on Application-defined TLVs
I/F

## Slide 15
Analyze, Optimize and Monetize your Network

## Slide 16: Clock Network Graph

## Slide 17: Clock Network Summary

## Slide 18: Clock Performance

## Slide 19: Port Performance

## Slide 20: Clock Details