## Slide 1: Secure Timing Architecture for Untrusted Edge Systems
MIRONOV VYACHESLAV fanwar@umass.edu
In collaboration with my PhD advisee, Adeel Nasrullah

## Slide 2: An Edge Platform
2
Hardware
Operating System
Application
Information flow
Information flow

## Slide 3: Networked Edge System
Cloud
Edge
Multi Tier
Multi Modal
Application
OS
Hardware
Application
OS
Hardware
Network Fabric
Physical World

## Slide 4: Untrusted Edge System
Cloud
Multi Tier and Delay prone
Multi Modal and Diverse
Edge
Network Vulnerabilities
Machine Learning
Database
Drone
Environmental Sensors
AR/VR
Headsets
Physical World

## Slide 5: Vulnerabilities in Time
Causes
Malicious delays
Inconsistent rates
Induced drifts
Consequence
5
Time discontinuities, Fuzzy Time

## Slide 6: Attack Strategies
Absolute Reference time
Time Source 1
6
No Attack

## Slide 7: Attack Strategies (1)
Absolute Reference time
Time Source 1
7
Offset Manipulation
Jump Time Arbitrarily
Fuzzy Time

## Slide 8: Attack Strategies (2)
Absolute Reference time
Time Source 1
8
Rate Manipulation
Increase Time Advance Rate
Error Accumulation over time
Effect on a Single Time Source:

## Slide 9: Attack Strategies (2)
Absolute Reference time
Time Source 1
Increase Time Advance Rate
Decrease Time Advance Rate
Time Source 2
Rate Manipulation
error = 2 error = 4
error = 0
9
Relative Effect on Two Time Sources:

## Slide 10: Time Attack Consequences
Location theft
Grid Attack
Forge Timestamp
10
Activity Misclassification

## Slide 11: CARLA Simulator Network Time Attack
11

## Slide 12: Attack on ARM Trustzone “Trusted” Time
12

## Slide 13: Problem and Proposed Approach
1
3

## Slide 14: Time Transfer for Heterogeneous Devices with Sensor Clocks
Goal:
Make a case for sensing channels to securely transfer time across heterogeneous Commercial Off The Shelf (COTS) devices at a low bandwidth and compute cost
Explore alternative signals to traditional networking packets, and alternative channels for time synchronization

## Slide 15: Sensing for Synchronization - Prior Work
t
Voltage
16.67 ms
t
Light Intensity
8.33 ms
No Packet Exchange
Support multiple Radios
Low Power Consumption
State of the art work
Electromagnetic Waves
Fluorescent Light

## Slide 16: Sensing for Synchronization — Limitations
t
Voltage
16.67 ms
t
Light Intensity
8.33 ms
Electromagnetic Waves
Fluorescent Light
Customized Hardware
No support for diverse sensors
Existing sensing based synchronization lacks support for commodity sensors

## Slide 17: Problem Statement
How to build a universal sensing based time synchronization solution for resource constrained commercial off the shelf heterogeneous devices?
No Custom Hardware Requirements Heterogeneous software, network and radio support
Low energy, bandwidth and computational requirements

## Slide 18: Our Approaches
Microphone
Optical
Sensor
Grid ENF Edge Server
Light
Audio
Microphone
Optical Sensor
IMU
Active Sensing
Passive Sensing

## Slide 19
Harvesting Ambient Events to Synchronize Time across heterogeneous IoT Devices (HAEST)
Passive Sensing Approach

## Slide 20: HAEST - Principle Idea
Microph
one
Optic
al
Sens
or
IM U
Door Opened
Door Closed
Optical Sensor
Door Opened
Door Closed
Microphone
IMU
Device Clocks
A
t M
A
t I
A
t O
B
t O
B
t I
B
t M

## Slide 21: HAEST - Research Challenges
Event Detection: Lightweight (throughput > 1k samples/sec), Universal (shared algorithm) and Scalable (No Manual Calibration)
  Cadence: throughput 33 samples/sec with a dedicated deep learning model
Delay Adjusted Clock Sync: a single event is detected with a delay across sensor pair
  Ambient signals travel asymmetric distances towards the pair
  Signals may have drastically different propagation speeds
Network-wide Sync: all sensors in a network do not observe events in common

## Slide 22: Research Challenge 1
Event Detection — Intuition
S
ensor Data
Encodings
Sensor Data
Sensor Data Distribution
Auto- encoders
Distance Scores

## Slide 23: Event Detection
Sensor Data Vector
Encoder
Distance
Calculation
Local
Maxima
Events
Scalable: Auto- encoders training is unsupervised eliminating the need for manual calibrations.
Research Challenge 1

## Slide 24: Event Detection — Lightweight
Sensor Data
Vector
Encoder
Distance
Calculation
Local
Maxima
Events
8-bit integer ops
32-bit floating point matrix
Quantization
Research Challenge 1

## Slide 25: Event Detection — Universal
S1
S2
SN
Sensor Data
Batched Inputs
Unified Encoder
Specialized Encoders
Distance Calculation
Local Maxima
S1 Events
S2 Events
SN Events
Research Challenge 1

## Slide 26: Event Detection — tackling high data rates
Sensor Data
Vector
Encoder
Distance Calculation
Local Maxima
Events
SN
SN
Cascaded
Detection
Research Challenge 1

## Slide 27: Event Detection — putting it all together
S1
S2
SN
Sensor Data
Batched
Inputs
Unified
Encoder
Specialized
Encoders
Quantized Models
Distance
Calculation
Event Detection
S1 Events
S2 Events
SN Events
S
N
SN
Cascaded
Detection
Research Challenge 1

## Slide 28: Research Challenge 2
Delay Adjusted Clock Sync
1 meter
3 meter
Optical Sensor Delay:
1 meter
do =
3 x 108 meter/second
Audio Sensor Delay:
3 meter
do =
340 meter/second

## Slide 29: Research Challenge 2
Delay Adjusted Clock Sync
vs
drift =
k
Z
i=1
d(bini) dt
offset = 1
n
n Z
i=1
bin0
i

## Slide 30: Research Challenge 2
Delay Adjusted Clock Sync
Key Result Higher sampling frequency yields better clock estimates
Key Result Some sensor types on a platform out perform the others
Key Result Inverse relationship between event occurrence rate and clock error

## Slide 31: Research Challenge 3
Network-wide Synchronization
Markov Clustering Algorithm
for node :
for edge :
delete i f edge! = max( freq)
31
for node :
for edge :
delete i f edge! = max(events)

## Slide 32: Overall HAEST Design
 |  | s
En | Train Sensor coder | 
Data Collection
Base Encoder Model
Base
Encoder Model
Base
Encoder Model
Base
Encoder Model
Base
Encoder Model
Base
Encoder Model
Data Streaming
Sensor
Encoder
Inference
Sensor
Bootstrapping Phase
Synchronization Phase
Sensor Network: Sync Pairs
Inference
Mutual Event Count
Network Sync
Event Detection
IoT Devices
32
Gateway
Clock Parameter Estimation
Clock Pair Sync
Detected Mutual Events

## Slide 33: Evaluations
33
Heterogeneous commodity devices
  ESP32 Things: 32-bit dual Core, WiFi/BLE enabled, hardware time- stamping, RTOS
  STK 2650: 32-bit single Core, BLE enabled, software time-stamping, RTOS
FLORA: 8-bit single core, Serial Communication, software time-stamping
Heterogeneous commodity sensors
  IMU, optical and audio
Event detection results using data-sets: UCI HAPT (IMU) and DCASE 2016 (Audio)
Clock parameter estimation: characterization of frequency, sampling rate and
sensor type affects on clock drift
Case Studies: Smart Home and WBAN study to evaluate network wide synchronization performance
Performance comparison with NTP

## Slide 34: Case Study: Smart Home
34

## Slide 35: Case Study: Results
Intra-cluster sync error
35
Inter-cluster sync error
Key Result
We achieve an average error of few milliseconds and best case error is under a millisecond.
Key Result
On average inter-cluster sync errors are greater than intra-cluster errors.

## Slide 36: NTP Comparison
NTP over Serial Connection
36
NTP over BLE Connection
Key Result
We achieve better mean error and spread than NTP over both the serial and BLE connection while consuming less power.
NTP consumes upto 36% more power.

## Slide 37: Problem and Proposed Approach
3
7

## Slide 38: Questions