## Slide 1: OCP-TAP SESSION 6.12.2023 5G BASED PNT USING TV TRANSMITTERS

## Slide 2: THE PROBLEM
GNSS is the „gold standard“ for uncountable timing users with sub-1µs demand
  free-of-charge
  afordable receivers
decent accuracy
often the source of PTP masters
  Few clients have direct PTP link to NIST, PTB, …
What if GNSS is not available?
  PTP from an atomic clock ensemble
What if you can‘t easily connect to the ensemble with PTP?
  Or you‘re in motion?
Could we use another RF signal as a time source?
NIST
PTB
UTC
USNO
GPS
PTP
master
PTP
client
PTP
client
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters

## Slide 3: BROADCASTING TIME – TECHNOLOGIES, ACCURACIES
GNSS performance:
  few ns
Long wave, DCF77 in Europe, WWVB in US, JJY in Japan, …
  few µs in best case, cheaper receivers: tens of µs
    https://www.ptb.de/cms/fileadmin/internet/fachabteilungen/abteilung_4/4.4_zeit_und_frequenz/pdf/2004_Piester_-_PTB-Mitteilungen_114.pdf
Accuracy limited by narrow bandwidth
Broadcast systems:
  FM (RDS) ~100 ms
  DVB-T2 ~0.3 µs on PHY, but not UTC traceable
    up to 1 s (!) error for UTC time in payload
Synchronized Delivery of Multimedia Content over Uncoordinated Broadcast Broadband Networks, Concolato et. al
Cellular 5G networks
  5G TDD requires 1.5 µs vs. UTC
  In practice: 50 ns to 1.5 µs
*) UTC broadcast is optional – often not sent
Difficult to assure performance of 10000+ base stations
PTP-WR
GNSS
DCF77 WWVB
DVB-T2 FM UTC Time RDS
ps
ns
µs
ms
s
NTP
PTP
5G cellular*
???
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters

## Slide 4: USING TV SIGNALS AS A TIME SOURCE?
Could be built independent of GNSS
  Less vulnerable to solar storm, jamming, spoofing
High power signal (100kW to 1000kW ERP)
World-wide UHF band (~450-600/700 MHz)
Electricity backup at many transmitters
Very high availability
Infrastructure is already in place
6-8 MHz bandwidth  many GPS receivers don‘t use more either
~100 towers to cover a country like Germany
  Monitoring and synchronization is manageable
Cheap directional antennas – hard to jam
< 100 $
Amplifiers for a 1 MW transmitter

## Slide 5: THREE CHALLENGES
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
Signal for afordable timing receivers
  There is not „the single“ digital TV standard for the world
  Should have a lower-layer UTC timestamp
  Should not be proprietary
Improve the accuracy of transmitters for sub-µs use cases
Distributing GNSS-independent time to each TV transmitter

## Slide 6: 1 – THE SIGNAL
Cíeated with Bing image cíeatoí

## Slide 7: DIGITAL TV STANDARDS
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
Digital TV transmitters are software-defined-radios
They can be re-configured for ATSC 3.0, DVB-T2, ISDB-T, DTMB, feMBMS
  There is not a global standard
  Which one to use?
    We chose 3GPP feMBMS (currently in trial stage)
    Another independent project chose ATSC 3.0
    Essentially any of these standards could be extended
to carry a UTC time stamp

## Slide 8: FEMBMS?
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
feMBMS: „LTE for Broadcasting from TV towers“
  Standard by 3GPP (the standardization body that brought you 4G and 5G)
    Essentially some kind of LTE signal
  offers the timing and positioning features from the 3GPP „toolbox“
    e.g. a UTC timestamp normal phones can read already
  Enabling low-cost mass-market receivers (Essentially a LTE modem with some SW modifications)
    SW-Modified smartphones able to receive feMBMS signals already today
      https://youtu.be/03h8dJTIEUo?si=xB8EjKTiNIY5z5PI&t=76

## Slide 9: DIFFERENCES LTE VS. FEMBMS SIGNAL
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
 | Normal LTE | feMBMS
Uplink | yes | No
Subcarrier spacing | 15 kHz | 15 kHz, 2.5 kHz, 1.25 kHz or 0.625 kHz
Cyclic Prefix | 16.67µs | 400µs, 800µs, 1600 µs
UTC time broadcast | SIB16 | SIB16
Transmitter location broadcast | standardized | Can be added
Application | Cellular network | Broadcasting towers

## Slide 10: HOW DOES THE LTE/FEMBMS SIGNAL LOOK LIKE?
OFDM signal
5-8 MHz Bandwidth
15 kHz subcarrier spacing (2.5, 1.25, 0.625 also allowed)
10 ms Frame length
Several pilot signals:
  Primary Synchronization Signal
  Secondary Synchronization Signal
  Cell-Specific Reference signals
Receiver reads time information from System Information Block:
  MIB: Master Information Block fundamental data of cell
  SIB1: Containing info where to find the other SIBs (i.e. SIB16)
  SIB16: UTC time of frame start
    Including leap seconds vs. GPS
Source: http://paul.wad.homepage.dk/LTE/lte_resource_grid.htm
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters

## Slide 11: HOW TO GET THE PRECISE UTC TIME FROM LTE/FEMBMS
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
Specified in 3GPP 36.311
SystemInformationBlockType16 (simplified)
  timeInfo
    timeInfoUTC INTEGER (0..549755813887),
    dayLightSavingTime BIT STRING (SIZE (2))
    leapSeconds INTEGER (-127..128)
    localTimeOffset INTEGER (-63..64)
“timeInfoUTC: Coordinated Universal Time corresponding to the SFN boundary (…). The field counts the number of UTC seconds in
10 ms units since 00:00:00 on Gregorian calendar date 1 January, 1900 (…). NOTE 1.
NOTE 1: The UE may use this field together with the leapSeconds field to obtain GPS time”

## Slide 12: HOW ABOUT TX LOCATION?
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
TX location: posSIB
  However, small gap in 3GPP feMBMS standard: would require a change request to be standard compliant for broadcasting mode
Specified in 3GPP 37.355:
  NR-UEB-TRP-LocationData
    nr-trp-LocationInfo NR-TRP-LocationInfo-r16,
    nr-dl-prs-BeamInfo
Can encode TX location, incl. antenna phase center, beam direction

## Slide 13: TRANSMITTER - ENHANCEMENTS
Implemented SIB16 for UTC timing
Added PRS
Planned: Add posSIBs: Identified necessary extensions in 3GPP for broadcast mode

## Slide 14: TEST RECEIVERS
Receiver A: R&S TSME Measurement receiver
  ~10 ns TDOA accuracy, ~15
ns TOA accuracy
  PPS-out for timing applications
Receiver B: OBECA Open- source SDR based on LimeSDR
  Affordable “starter-kit” for
universities, students, …
  No PPS out

## Slide 15: 2 - ACCURACY
12/06/2023 5G based PNT Using TV Transmitters
Lab test setup used to improve the jitter
TV transmitter #1
TV transmitter #2
TV transmitter #3
No amplifiers, few Watt max power
PC connected to receiver
TSME receiver (not visible here)

## Slide 16: TRANSMITTER SEGMENT
Simplified TV transmitter diagram including measurement devices

## Slide 17: TRANSMITTER ACCURACY – STATUS QUO
The transmitter’s OXCO error is the main error source of the RF signal’s time inaccuracy
Error contribution ~ 100 m
(300 ns)
Other Periodic and systematic errors visible
Targeted Optimizations
during this project:
  Improve OCXO control
  Improve SFN regulator
Accuracy-Analysis of RF Signal jitter (before this project)

## Slide 18: OCXO BYPASS
If OCXO is bypassed, largest error removed, but still periodic 100 ns error visible
SFN regulator causes periodic error. If mitigated, we would expect less than 50 ns error
Residual error Timing error Systematic effect
Residual error: 50 ns

## Slide 19: OCXO AND SFN OPTIMIZATION
Timing error < 40 ns
Remaining timing error (< 100 ns) after improvement of OCXO PID controller, without bypass
Remaining timing error ( < 40 ns) after improvement of OCXO PID
controller and SFN regulator

## Slide 20: SUMMARY TRANSMITTER IMPROVEMENTS
TV transmitter jitter
reduced from 300 ns to 40 ns
Further improvement technically possible
SW update

## Slide 21: FIELD TESTS – VIENNA TEST BED
3 HPHT sites from ORS in Vienna:
  TX1: Kahlenberg, ca. 40 kW ERP
  TX2: DC Tower,
ca. 10 kW ERP
  TX3: Liesing, ca. 10 kW ERP
  UHF band, 666 MHz
  5 MHz bandwidth
TX1
TX2
TX3
TX1
TX2
TX3

## Slide 22: FIELD TESTS – URBAN / SUBURBAN ENVIRONMENT
Scatter Plot at Küniglberg

## Slide 23: FIELD TESTS – STATIC LOCATION SCATTER PLOT
Slowly moving due to uncompensated clock drift of non-ideally synchronized transmitters
  Effect of external GPSDO, not the transmitters themselves
Inaccuracy due to transmitter jitter is lower, estimated ~30 m
50m radius

## Slide 24: FIELD TESTS – STATIC MEASUREMENT AT ORF HQ
Receiver at the rooftop of the ORF headquarter at a fixed position during the measurement
Overall scatter cloud
slowly moved over the time
First 20 minutes of the test were also evaluated. The remaining uncertainty was only 11 m for 50% and 24 m for 95% of the valid fixes.

## Slide 25: 3 – NETWORK SYNCHRONIZATION
Cíeated with Bing image cíeatoí

## Slide 26: HOW TO SYNCHRONIZE?
TV transmitters have a broadband link to playout centers
Historically: P2P-Microwave
Nowdays: sometimes fiber
  More often still microwave
If Fiber:
  PTP(WR)
If Microwave:
  Proprietary systems for ns-level sync available
  PTP-over-microwave:
    Unknown performance
    Feedback from audience?
Source: http://www.dvb-t2hd.de/

## Slide 27: HOW TO SYNCHRONIZE?
Hypothetical P2P microwave backbone for Bavaria
Good coverage for sub µs
time
High-end users could also directly tap the backbone
  For ns-level time
Hypothetical timing backbone
between transmitters
Potential direct tap for a high end user
Source: http://www.dvb-t2hd.de/

## Slide 28: SUMMARY
Using an improved network of tightly UTC-synchronized TV transmitters
2nd source beside GNSS for PTP masters
  ~40 ns accuracy possible with SW updates
Accuracy close to GNSS performance
  Much better than long wave signals
  Much cheaper than a fiber link with PTP from NIST
  Supporting mobility
NIST
PTB
UTC
USNO
GPS
PTP
master
PTP
client
PTP
client
TV
network
PTP-WR
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
GNSS
DCF77
WWVB
DVB-T2 FM UTC Time RDS
ps
ns
µs
ms
s
NTP
PTP
5G cellular
TV Signal

## Slide 29: QUESTIONS, FEEDBACK?
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
Thank you for your attention!
Project was co-funded by ESA NAVISP Element 2

## Slide 30: BACKUP SLIDES

## Slide 31: EXCURSION: CELL SIZE, CYCLIC PREFIX AND SUBCARRIER SPACING
If the distance between two neigboring towers increased, the time difference of their signal at receiver increases
In a single-frequency-network, all transmitters send same signal  multiple „echos“ at receiver
If all echos are within the cyclic prefix, signal is improved by each echo
TV towers are further apart than cellular towers  larger cyclic prefix desired
If cyclic prefix is extended, less time for data symbols
Extend duration of OFDM symbols and have less symbols per frame
  Need to reduce subcarrier spacing in return
Less subcarrier spacing: Less doppler resilience
https://5g-xcast.eu/wp-content/uploads/2019/05/TBC_NRMBMSforTB_2019.pdf
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters

## Slide 32: THE SAME TIMING RECEIVER COULD USE TV AND CELLULAR SIGNAL AS SOURCE
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
An feMBMS timing receiver could easily also receive LTE signals with time information

## Slide 33: HOW ARE TV TRANSMITTERS ORGANIZED
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
In Europe, Africa and most of Asia:
  ITU decided a frequency scheme (GE06) that assigned frequencies to regions, in a way that neighbor regions are not affected.
  One region might be served by a Single-Frequency network instead of a single transmitter
  Regions are using different frequencies
  E.g. Germany uses the whole 450-690 MHz range, but each region has only six 8 MHz channels that can be used
In US, FCC decides on TV stations
  Recently, spectrum was re-packed. Less use of SFNs, more high-power transmitters

## Slide 34: WHY NOT DIRECTLY USING A CELLULAR NETWORK‘S TIME?
Rohde & Schwarz
12/06/2023 5G based PNT Using TV Transmitters
Dependency on electric grid
  Most cell networks have only limited backup power, e.g. for 30 minutes
More difficult and costly to guarantee a time synchronization in 10000+ basestations, vs. ~100 TV
towers (taking Germany as an example)
But: If your cellular network operator offers you SIB16: Why not?