## Slide 1: The “BIG” Precision Time Measurement Picture

## Slide 2: Part 1 PTM in context: Why do we care?

## Slide 3: PTM – What’s the BIG deal?
Let’s start by talking a little about what problems PTM solves and why PTM is a critically important technology that is poised to receive a lot of attention in the short term.
I’ll do that by talking about what the world currently looks
like.
It is not well understood how big a problem the lack of hyper accurate synchronisation is in your average datacenter server, nor why in the short term PTM as a technology is likely to get a lot of attention.

## Slide 4: This works great: sub 10ns accuracy - $40 NIC
P
H C
PHC
< 10ns accuracy
(Timebeat advanced filtering 2ns theoretical limit possible)
PHC
to
CPU
CPU

## Slide 5: This still sucks: Non-deterministic asymmetry
PHC
50ns – 2,500ns 50ns – 2,500ns
Even with filter algorithms the unknown latency characteristics of the
PCIe bus causes significant variance in the clock accuracy of the CPU
Congestion on the PCIe bus contributes to this
Changes in CPU p-state is a particularly difficult problem to overcome
Improving accuracy requires filtering that consumes considerable CPU
  A single server typically contains lots of PHCs
CPU
CPU
PHC

## Slide 6: How do we sync the CPU clock from a PHC? (without PTM)
Commonly the ioctl
“PTP_SYS_OFFSET_EXTENDED” is used
In the device driver for a particular NIC (or other PHC device) 3 timestamps are captured.
  Two from the CPU interleaved with one from the PHC
It is then assumed that the the interleaved PHC timestamp occurred halfway between the two CPU timestamps
This is frequently a “pretty terrible”™
assumption
To compensate it’s not uncommon to collect these timestamps many time concurrently and use minimum delta between T1a and T1b
  Because preemption happens in none-RT
operating systems etc
Clock Offset =
𝑇1𝑎+𝑇1𝑏 2
− T2
(xN)
T1a
T2
PHC
T1b
E
v e n t s
𝐵𝑒𝑠𝑡 𝑠𝑎𝑚𝑝𝑙𝑒: 𝑚𝑖𝑛(𝑇1𝑏1 − 𝑇1𝑎1, … 𝑇1𝑏𝑛 − 𝑇1𝑎𝑛)

## Slide 7: Classic Test: Variance of distribution != Offset
To understand why the offsets displayed by phc2sys for instance in no way reflects the actual offset one can perform the test on the right.
It is not uncommon for the phase difference between the two PPS signals to be hundreds of nanoseconds even if the std.dev of 𝑃1 and 𝑃2 is no more than 20ns.
The reason is asymmetry as discussed in previous slide which has not been compensated for.
It can be statically compensated for, but this is not practical in large deployments with varying hardware builds.
PHC-A
Oscilloscope
Spectroscope∗
PHC-B
𝑷𝟏
𝑷
𝟐

## Slide 8: The absence of PTM is palpable
Intel XXV710-DA2T NIC with PPS daisy chaining capability
OCP-TAP Timecard connected with external loop to NVIDIA ConnectX-6 NIC

## Slide 9: Part 2 Applications: High Accuracy Timekeeping

## Slide 10: What Can we do with it (Why)?
Inside a Machine
  Precision Sync between devices on a system such as GPUs, NIC and CPU
Between Machines
  Correlate events (such as logs)
  Intermachine Telemetry (Compare Pipelines)
  Align and Calibrate (Reduce Tail Latency)
  Linearizability (Higher Precision Hybrid Logical Clocks for Consensus)
In a Network
  One-way latency (precise measurement of packet journey across the network)
  Congestion Control using deterministic traffic management

## Slide 11: What comes out of this?
Machine X
Machine Y
Pseudo
Entanglement
Machine X and Y are any two machines across the globe or inside a local network
Pseudo Entanglement: Probabilistic Entanglement of two Registers (Machine Y and Y) within the Windows of Uncertainty Window of Uncertainty: An ongoing estimation of a time interval that UTC (or TAI) sits inside it (with a given probability)
UTC of TAI
Time
WOU

## Slide 12: Time Precision and Applications
WR
PTP
NTP
Industry Standard Physical Clocks
Packet Latency
Userland (Globally) OS
Disk
Operations
PTP
Real Time Linux
Industry Platform
s
500ms 100ms 20ms 2ms 1ms 500us 250us 100us 50us 20us 5us 1us 500ns 100ns 10ns 1ns 100p 10ps 1ps
Packet Latency (P2P)
WR
NTP
INT
DC like a PC MMU
DDP
CCP

## Slide 13: Correlate Events Between Machines
Event 1234
Event 1235
Event 1236
Event 1237
Event 1238
Event 1239
Event 1240
Event 1282
Event 1283
Event 1284
Event 1403
Event 1404
Event 1405
Event 1406
Event 1407
Event 1653
Event 1654
Event 1655
Event 1656
Event 1657
Event 2044
Event 2045
Event 2046
Event 2047
Event 2048
Event 2049
Event 2050
Event 2051
Event 2077
Event 2078
Pseudo Entangled
Machine A
Machine B
Machine C
Machine Local Time
Machine Local Time
Machine Local Time

## Slide 14: Runtime Difference in a Pipeline
Machine A
Time Axis
Machine B
Machine C
Machine D
Pipelines
Machine A
Machine B
Machine C
Machine D
Machine A
Machine B
Machine C
Machine D
Machine A
Machine B
Machine C
Machine D
Epoch #1

## Slide 15: Tail Latency
Machine A
Time Axis
Machine B
Machine C
Machine D
Pipelines
Machine A
Machine B
Machine C
Machine D
Machine A
Machine B
Machine C
Machine D
Machine A
Machine B
Machine C
Machine D
Epoch #1

## Slide 16: Align and Calibrate Machines in a Pipeline
Machine A
Time Axis
Machine B
Machine C
Machine D
Pipelines
Machine A
Machine B
Machine C
Machine D
Machine A
Machine B
Machine C
Machine D
Machine A
Machine B
Machine C
Machine D
Epoch #1

## Slide 17: Precision Time
In the Last Centimeters
2023-04-12

## Slide 18: Precision Time is a Foundational Capability
Live A/V
Industrial / CPS
Conferencing
5G / Comms
Financial
Cloud
Automotive
AR/VR
and Gaming
Edge
Mobile Robots
Time Sync is required
[Sometimes
Deadlines too]
Time Sync required and Deadlines must be met
Where Time Bounds are Necessary for Correctness of the Application, Compliance, etc
HPC

## Slide 19: Time Synchronization Measurement Methodology
Network
Application
System Clock
“Now”
CPU Clock
(TSC)
Network Interface
Network Reference Clock
TGPIO
Application
System Clock
“Now”
CPU Clock
(TSC)
Network Interface
TGPIO
Hardware
Software
PCIe
PCIe
Oscilloscope / Logic Analyzer
offset

## Slide 20
Loaded, No PTM
Idle, No PTM
With PTM (loaded & unloaded)

## Slide 22: Using PCIe PTM to Capture Cross-Timestamps
System Time_1
Cross Timestamps, Captured Simultaneously
Sample Scenario:
Device Driver Triggers Cross-Timestamp
Device initiates PTM Request TLP to Root Complex
System Time is Returned (delays are compensated )
(PTM Time, PTP Time) returned to NIC Device Driver
Software “disciplines” Coefficients per clock: m (and c)
Switch
Computer
System
Other I/O Device
NIC
System Time
PCIe Root Complex
Delays over PCIe links and through Switches are corrected
PTP Network Time
LAN
Cross Timestamps  ‘m’ and ‘c’ Coefficients
System Time_2
Other I/O DeviceTime
From PCIe Specification

## Slide 23: PTM with a PCIe Switch
Root Complex
PTM Leader Time
Switch
Endpoint A
Endpoint B
Endpoint A Initiates PTM Request upward
  At the request of Software
  Or on its own
Switch initiates PTM Request upward
Root Port Responds with the time downward
  Delays measured and compensated
Switch Responds with the time downward
  Delays measured and compensated
Endpoint knows the PTM Leader Time
Delays measured and added to the PTM Time
Link delays, PCIe SERDES Delays
Duration between 3. to 4. above

## Slide 24
1
PTM – device side

## Slide 25: Peripheral devices & sync
Synchronization signal originates from the outside anyway
Multiple ways to get to the platform:
  PTP
  SyncE (+phase)
  GNSS
  PPS
  refclk input (+phase)
CPU
peripheral device 1
peripheral device 2
2

## Slide 26: Is it enough?
tbh it was, for a long time
there was always some way to coarsely synchronize CPU and other peripheral devices
precise synchronization was the domain of specialized/embedded/purpose-built systems
even most of the early usecases for commodity platforms were network-oriented (TSN, 5G fronthaul, …)
  and so could be offloaded to the peripheral device
more usecases started popping up, often with demands for CPU/non-network timestamping
  schedulers (e.g. 5G)
  processing of realtime data (e.g. Holoscan sensors)
  time-driven CPU applications (e.g. distributed databases)
  time-driven GPU applications (e.g. distributed rendering)
  consistent profiling of distributed applications

## Slide 27: Intra-Platform Distribution How to deliver synchronization to other devices in the system?
Option 1:
Each device gets outside connection and is independently synchronized to external signal
For network-derived signals, even non-networking devices need a network port
Option 2:
Out-of-band: extra synchronization cabling between devices
E.g. daisy-chain PPS signals of all network adapters
Option 3:
In-band: over PCIe bus
with/without support for PCIe synchronization features

## Slide 28: Quick segue time uncertainty
New time-sensitive applications require estimating local clock uncertainty
We never had a way to be sure about time on x86
  which is problematic for True-Time-like APIs
Can always assume worst case, I guess?
But what is the worst case, really?
Tested with NIC1 -> CPU -> NIC2 -> PPS Out -> PPS In
  saved $$$ on oscilloscopes/”spectroscopes” 
Measured 100s of nanoseconds
Suspected smoothing effect of the CPU in the middle
NIC 1
CPU
NIC 2
PPS
phc2sys
phc2sys
monitor PPS In events (testptp)
generate PPS Out signals (testptp)
5

## Slide 29: how device <> CPU sync works today
SYS_pre DEV
= read(SYS.clk)
= read(DEV.clk)
SYS_post = read(SYS.clk)
SYS = (SYS_pre + SYS_post) / 2 DEV_SYS_offset = (DEV – SYS)
kernel
SYS.clk
DEV.clk

## Slide 30: More like…
kernel
SYS.clk
DEV.clk
The PCIe wonderland

## Slide 31: Test platform schematic
SPR-based server
ConnectX-7
Oscilloscope
Keysight DSO-X 3034A
ch1
ch3
Port 0
Port 1
ppppss
out
TGPIO
iperf client
x4
iperf client
iperf client
iperf client
iperf client
iperf server
iperf client
iperf client
iperf client
iperf client
iperf client
iperf client
iperf client
iperf client
iperf client
iperf client
iperf client
iperf server
iperf client
iperf client
iperf server
iperf client
iperf client
iperf server
x4
~120
Gbps
sys clk

## Slide 32: NIC → CPU sync 11-hour run, no PTM (yet)
Adjust CPU time 8 times/second
For each adjustment, measure CPU/NIC time diff 15 times, use “luckiest” measurement
iperf - loaded system CPU/NIC time error:
min: | -635.0 | [ns]
max: | 1713.0 | [ns]
pk-pk: | 2348.0 | [ns]

## Slide 33: Let’s talk about PTM
simple spec
special PCIe messages
HW timestamping of ingress/egress
distributes “master” time [in nanoseconds]
  PTM “master” time doesn’t have to be the
wall-clock-external-reference-time
  It’s a “ruler” by which every device in the platform gets to measure the passage of its local time
NVIDIA Connect-X has it
  need 2 to tango

## Slide 34: What it takes on the device
PTM (Requester) MVP for any peripheral device:
  a counter
  ability to send PCIe messages with configurable opcode
  PCIe logic to recognize special opcodes and snapshot the counter when messages with those special opcodes are sent/received
    In flit mode (gen 6+), it’s even simpler
  some way to communicate information to the host
  R/W PCIe capability register
To illustrate, my entire implementation for PTM is ~300 LOC, including documentation

## Slide 35: NIC → CPU sync with PTM, 16-hours run
Adjust CPU time 8 times/second
For each adjustment, measure time difference between CPU and NIC once
(iperf) loaded system CPU/NIC time error:
min: | -8.5 | [ns]
max: | 55.5 | [ns]
pk-pk: | 64.0 | [ns]

## Slide 36: Are we done? device drivers: not quite
Though basic support is available in upstream Linux, there are a few flaws
Device driver is asked to cross-timestamp with system clock. What is the relation between PTM Master Time and system clock?
  Current upstream code assumes ART derivative is used for PTM Master Time.
  And that CLOCK_REALTIME is based on TSC.
  And that TSC is related to ART.
PTP_SYS_OFFSET_PRECISE API allows cross- timestamping device/system clocks.
  What about device/PCIe switch?
  PCIe switch can act as a sort of “boundary clock”
  Maybe Linux kernel needs an explicit notion of “PTM Master Time” and its constant relation with CLOCK_REALTIME (in case TSC/ART is used)
13