## Slide 1: SyncESMC
ITU-T G.781 Multi-Clock ESMC Implementation
©2022 SyncMonk Technologies | www.syncmonk.net | info@syncmonk.net

## Slide 2: Introduction
SyncMonk is an early stage bootstrapped startup founded in 2020. We are based in Bangalore, India with main focus on time synchronization services and products. SyncMonk provides complete integration services to Telecom, Networking and Semiconductor companies.
SyncMonk believes in innovating things and is working on the Time Services portfolio including software and hardware solutions.
Solutions offered by SyncMonk are:
  SyncESMC v1.0 an ESMC implementation based on ITU-T standard,
  FishEye - Set your Vision Clock Monitoring tool for sync and time services
  SyncPTP ptp stack optimized and in compliance with IEEE 1588-2019 standard and respective profiles.
www.syncmonk.net| info@syncmonk.net

## Slide 3: Agenda
Overview
Why SyncESMC
Architecture
  Design GOALS
  Configuration
  Packet Engine
  ESMC State Machine
  Hardware Abstraction Layer (HAL)
External Interface
FishEye
Demo Video
www.syncmonk.net| info@syncmonk.net

## Slide 4: Overview
ESMC is a Logical Channel which transmits SSM information.
The SSM information determines the Quality level of EEC.
It is based on ITU-T G.8264 (03/2018) and ITU-T G.781 (04/2020)
Ethernet SSM is ITU-T-defined Ethernet Slow Protocol.
www.syncmonk.net| info@syncmonk.net

## Slide 5: Synchronization Network Topology
www.syncmonk.net| info@syncmonk.net

## Slide 6: Why SyncESMC
Hardware Abstracted ESMC stack.
Compliant to G.781(04/2020) and G.8264 (03/2018).
Simplified Single Threaded architecture.
Interaction with PTP Stack (to support IWF)
Dynamic configuration support.
Monitoring with FishEye
Supporting Intel® E810XXVDA4T, Renesas® ClockMatrix™ 8A34001 and AuraSemi® 5508 PHC.
www.syncmonk.net| info@syncmonk.net

## Slide 7: Architecture
www.syncmonk.net| info@syncmonk.net

## Slide 8: Design GOALS
Single Threaded architecture.
Multiple hardware support using HAL
Multi Clock Support
External MUX for Input Signals
Futuristic design to support kernel driver support with minimal changes.
Interaction with multi-vendor PTP stacks.
In-built Support for Network configuration and Monitoring
Micro Service compatible for SONiC
www.syncmonk.net| info@syncmonk.net

## Slide 9: Configuration
Configuration Module has two modes:
Static Configuration Mode
  JSON-based configuration file.
  System boots up with the predefined configuration
  Configuration is majorly classified into
    Device
    Port
    Monitoring
Dynamic Configuration
  REST API
  Netconf-yang model for O-RAN
www.syncmonk.net| info@syncmonk.net

## Slide 10: Packet Engine
Packet Engine is involved with the interface-related activity.
Packet RX
Packet TX
Port Link up/ Link down Events (Network Link)
Packet filtering
Different types of Sockets and interface types are
Separated using packet engine library.
Raw Socket
UDS Socket
APIs
Packet Filter
RX
TX
Application
RTNL
Link
Events
www.syncmonk.net| info@syncmonk.net

## Slide 11: ESMC State Machine
Core of the ESMC stack.
Interacts with the Packet Engine, Configuration Engine, HAL
Decides to select the source port based on the Best Port Selection Algorithm. (Quality, Priority, Hops)
Handles the timer interrupts for Time outs for Hold off time, no activity on the port, Holdover timeout and Restore timers.
Interacts with HAL to configure the Hardware.
ESMC
State Machine
Packet Engine
Configuration
Timer
HAL
1
2
3
4
5
Packet Engine updates the packet metadata to Database.
Configuration can be updated run time
Timer-based events for TX packets, Holdover events, and RX timeout events.
Hardware events like LOS, OOF, PLL Loss
PLL ID and PLL input selection instructions to HAL.
www.syncmonk.net| info@syncmonk.net

## Slide 12: External MUX for Input Signals
Supports Multiplexing, where it can be configured for the maximum number of Sources available for a PLL and the maximum number of inputs which can be given to the PLL.
Runs an algorithm to select the best ports and based on priority programs the MUX.
Works with any of the available hardware where the number of inputs to PLL is more than the number of sources available. For e.g Broadcom XGS chips for Data Center switches
www.syncmonk.net| info@syncmonk.net
PLL
MUX
Source
Inputs

## Slide 13: Hardware Abstraction Layer
Hardware Abstraction Layer.
Hardware vendors can plugin their HAL functions to integrate with SyncESMC.
Ready for Kernel exposed APIs (in future) for controlling the hardware.
Hardware interrupt and status monitoring.
Multiple vendors’ PLLs can be controlled by the same stack.
HAL
(Hardware Abstraction Layer)
www.syncmonk.net| info@syncmonk.net

## Slide 14: External Interface
UDS socket can be used to interact with external applications
  PTP stack
    Seamless integration with any PTP stack over a UDS socket.
    SyncESMC can convert Clock Class to Clock quality as per G.8275.2 Annex F.
External Application Interfaces
  FishEye
  Configurations
www.syncmonk.net| info@syncmonk.net
SyncESMC
UDS
PTP
Exchange information on Application-defined TLVs
I/F

## Slide 15
Analyze, Optimize and Monetize your Network

## Slide 16: Clock Network Graph

## Slide 17: Clock Network Summary

## Slide 18: Clock Performance

## Slide 19: Port Performance

## Slide 20: Clock Details