## Slide 1: Window of Uncertainty
Ahmad Byagowi

## Slide 2: Motivation
Distributed applications may require to know the time sync error bound in order adjust their performance accordingly.
Linearizability as a requirement
Parallel to serial pipelines
One way latency
Precision Time Based Scheduling and Routing
Realtime Indication of Precision Time Sync System Performance
Precision Time Sync [components] Fault Detection

## Slide 3: Overview
PTP delivers time to the end nodes from the Time Server [aka GM]
End nodes need to estimate/predict the error bound
Time Server provides the end nodes with the error bound of its service
Error bound can be separated in two parts; precision and accuracy
Precision is based on the offset variance perceived by the end node
Accuracy is based on the agreement with other peers

## Slide 4: Quick Reminder on Precision vs. Accuracy
Not Accurate
Not Precise
Accurate
Not Precise
Not Accurate
Precise
Accurate
Precise
Reference

## Slide 5: Formulation
Clock synchronization requires processes (p1, p2, p3, … pn) to bring their clocks as close as possible together by using communication between them.
For process pi, the adjusted clock of a process pi AC(t)i is a function of the hardware clock HC(t)i and a variable adji
The synchronization process in pi adjusts the value of adji and thus changes the value of AC(t)i
Error bound of γ is defined by achieving |AC(t)i-AC(t)j| ≤ γ for any given i and j representing processes pi and pj
For every pi participating in clock synchronization, γ is at least ε(1-1/n) where ε is the uncertainty in the message delay [Lundelius and Lynch 84]
Assuming symmetry for the error bound γ we can write γ = (2(ε/2)+(n-2)ε)/n

## Slide 6: The Challenge in Sync Over the Network
Synchronizing Clocks in the Network over the noisy process of timing the packets.
Dij = Estimated difference between the physical clocks of pi and pj as estimated by pj
Δrx = True difference between a process px and the Time Server (or reference)
Show |ACi(t)-ACj(t)| ≤ ε(1-1/n)
|ACi(t)-ACj(t)| = |(HCi(t) + adji) – (HCj(t) + adjj)|
= (1/n)|Σ((Δri - Δrj) – (Dri – Drj))| ≤ (1/n) Σ |((Δri - Δrj) – (Dri – Drj))|
≤ (1/n) (2ε/2 + (n-2)ε) = ε(1-1/n)

## Slide 7: Estimation of Precision
Not Accurate
Not Precise
Accurate
Not Precise
Not Accurate
Precise
Accurate
Precise
Reference

## Slide 8: Precision
Precision is based on the sync variance perceived by the end node
End node is performing sync using a servo via the fabric of the network
Past offset changes determine/estimate the precision

## Slide 9: Schematic of Time Sync across the Network
Open Time Server (a.k.a. GM)
NIC
TC
TC
TC
TC
TC
TC
TC
End node
NIC
Network Fabric
Servo
Oscillator
App

## Slide 10: Law of total variance
Open Time Server (a.k.a. GM)
NIC
TC
TC
TC
TC
TC
TC
TC
End node
NIC
Network Fabric
Servo
Oscillator
App

## Slide 11: Open Time Server Error Bound
Open Time Server (a.k.a. GM)
NIC
GNSS
MAC

## Slide 12: Experiment
Front End NIC
Network (TCs)
End Node
NIC
Ideally!
STD[E2E]≃90ns

## Slide 13: Estimation of Variance and Stationarity

## Slide 14: Running Variance
Notes: Make is symmetric

## Slide 15: Estimation of error bound (WOU)

## Slide 16: Temperature Aware Error Bound
Monitor frequency adjust versus present oscillator temperature
Monitor temperature changes
Estimate upcoming changes of frequency based on temperature changes
Adjust the ratio between relying on existing model vs observation
  Model in this case is the hold over
  Observation in this case is a single clock sync episode

## Slide 17: Estimation of Accuracy
Not Accurate
Not Precise
Accurate
Not Precise
Not Accurate
Precise
Accurate
Precise
Reference

## Slide 18: Estimation of Accuracy
Based on Linearizability test
Estimation of statistical specificity
  How specific is it to find a machine that is not linearizable
This method is optimized for a TC only implementation
  Can be extended to BC included implementations
Each node seeks feedback from a random peer
  Decentralized
A scrolling history of linearizability tests with random peers determines the current estimate of accuracy

## Slide 19: Estimation of Accuracy
Time Server
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
OC
OC
OC
OC
OC
OC

## Slide 20: Rogue Transparent Clock
Time Server
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
TC
OC
OC
OC
OC
OC
OC
Not applying CF
Issues with LO
All the subsequent chain gets affected

## Slide 21: Accuracy Scenarios

## Slide 22: Accuracy Scenarios

## Slide 23: Accuracy Scenarios

## Slide 24: Conclusion
Time Sync Error Bound is an estimation process
The current state is determined by scrolling over the past observations
Sensory information like temperature monitoring can improve the estimation
Precision and Accuracy should be identified and calculated separately